## Slide 1
Coastal Bend Air Quality
Particulate Matter & VOCs — a Coastal Bend Briefing
PM2.5
Fine particulate matter
PM10
Coarse particulate matter
Prepared by Aidan Meyers · Melaram Lab team briefing · For internal use
Notes: Opening slide. Frame the deck: this is a Melaram-Lab-internal educational briefing on the three pollutants Aidan is now responsible for after the task redistribution — PM2.5, PM10, and VOCs. Coastal Bend focus per Dr. Melaram's guidance. The v0.3.7 EPA hybrid was retired in v0.4.0 and we now run against TCEQ TAMIS as sole source. Deck goal is not to argue a hypothesis — it's to align the team on what each pollutant IS, HOW it's measured, WHY the NAAQS look the way they do, and what specifically is in our database for each. Pace ≈ 90 seconds per slide; total run ≈ 90 min if delivered live, ~30 min if read individually.

## Slide 2
CONTEXT
Why this briefing exists
The problem
When we wrote up the Corpus Christi time-series manuscript, we reported FRM/FEM in a table without commenting on what they meant or how they change what we can compare across sites and years.
Instruments were also being replaced mid-study without our tracking which sites, when, or why. Reviewer comments surfaced this — we don't want that experience again.
Purpose of this briefing
Plain-English definitions of PM2.5, PM10, and VOC species
The chemistry & devices behind every FRM and FEM we see
Every AQS parameter code + method code appearing in our data
NAAQS values, when they changed, and why
Peer-reviewed health effects context (not analysis — background)
Sensor changes over 2015–2025 at Coastal Bend sites
Weather–pollutant relationships from the literature
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
2 / 60
Notes: Set expectations. This is a groundwork briefing — not a results deck and not a manuscript draft. The trigger was the Jasmine/Manasa/Aidan meeting where we acknowledged that our v0.3.7 time series manuscript didn't adequately explain FRM vs FEM, didn't comment on mid-study instrumentation changes, and didn't propagate that context into the NAAQS + modeling conclusions. This deck brings the whole team to a shared baseline before we build anything downstream. Content is drawn from EPA AMTIC, 40 CFR Part 50, TCEQ TAMIS documentation, and peer-reviewed literature (cited in the References section).

## Slide 3
AGENDA
What we'll cover
1
Study context & pipeline
Coastal Bend counties, data flow, sites
4–7
2
Reference-method foundations
FRM vs FEM, AQS codes, units, sensor evolution
8–15
3
PM2.5 — fine particulate
Composition, health, NAAQS 9 µg/m³, BAM, FDMS
16–30
4
PM10 — coarse particulate
Sea salt, Saharan dust, 150 µg/m³ 24-hr, hi-vol
31–40
5
VOCs — volatile organics
PAMS, AutoGC, TO-15, HAPs, ozone precursors
41–54
6
Synthesis & references
Cross-pollutant table, next steps, bibliography
55–60
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
3 / 60
Notes: Six sections. Sections 1-2 are shared background — everyone should read these regardless of which pollutant they own. Sections 3-5 are the pollutants Aidan took at the last team meeting (PM2.5, PM10, VOCs); Manasa now covers ozone + CO; Jasmine covers SO2 + NOx. Section 6 is the bibliography — every peer-reviewed claim in the deck is cited there. Total ~60 slides ≈ 90 min live or ~30 min self-read with notes.

## Slide 4
SCOPE
Coastal Bend — the pivot from full South Texas
From 13 counties → 7-county Coastal Bend focus
The v0.4.0 pipeline still stores all 13 South Texas counties for future work (Atascosa, Bexar, Cameron, Comal, Guadalupe, Hidalgo, Karnes, Kleberg, Maverick, Nueces, Victoria, Webb, Wilson).
Dr. Melaram scoped the next manuscript to the
Coastal Bend region only — TCEQ Region 14 — so we can:
Do site-by-site method interrogation without the Bexar site count exploding
Interpolate over a manageable geographic footprint
Use TCEQ hourly consistently (EPA daily forms don't work for us)
Reserve broader-scope work for follow-on papers
County | MSA / region | Aidan's sites*
Nueces | Corpus Christi | 6 (incl. Palm VOC)
Kleberg | Kingsville | 1
San Patricio | Corpus Christi–Portland | TCEQ CAMS (limited AQ)
Aransas | Rockport / Aransas Pass | TCEQ CAMS (limited AQ)
Refugio | Refugio | sparse
Bee | Beeville | sparse
Jim Wells | Alice | sparse
* Sites reporting PM2.5, PM10, or VOCs in v0.4.0 pipeline. Ozone / CO / SO2 / NOx also present at many of these sites but not part of Aidan's assigned pollutants.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
4 / 60
Notes: Explains WHY we narrowed from 13 counties to Coastal Bend. Original scope produced ~42 active sites and Bexar alone contributed 14 — too many to hand-audit method codes and sensor changes site-by-site. Coastal Bend gives us ~7 core AQ sites in Nueces + adjacent, letting us do the deep methods work we already know matters. Full 13-county data STAYS in the pipeline — we don't lose it. Follow-on papers can extend scope; this manuscript will not.

## Slide 5
PIPELINE
How the data gets to us
TCEQ TAMIS
51 raw .txt files
(AQS RD v1.6)
step_01b ingest
Concat A/B, ppb→ppm,
route by dur code
Parquet + Postgres
10 tables in aq.*
(2.4 GB Neon)
Colab / R / Python
Query, analyze,
interpret
9.77 M
Raw TCEQ rows ingested
from 51 .txt files
10
Tables in Neon aq schema
(criteria, VOCs, weather)
57
Distinct AQS parameter codes
(9 criteria + 47 VOC + 1 sparse)
~9 min
Full pipeline rebuild
local → parquet → CSV
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
5 / 60
Notes: One-picture summary of the pipeline. Left → right: TCEQ TAMIS dumps 51 pipe-delimited .txt files in AQS RD v1.6 format (each file = one site or one county-level VOC bundle). step_01b_ingest_tceq_raw.py parses those, applies A/B concatenation for sites like Heritage MS 480290622, converts TCEQ ozone from ppb → ppm (× 0.001), and routes rows by Sample Duration Code (7 or X → pollutant_daily_24hr table; everything else hourly). Downstream steps write partitioned parquet, then step_07 COPY-loads to Neon (10 tables, ~2.4 GB, 54 min). Anyone querying the aq schema in Colab is looking at that final COPY-loaded state.

## Slide 6
SITES
Coastal Bend AQ sites in our v0.4.0 pipeline
Nueces + Kleberg (schematic)
Not to geographic scale — see docs site for real map.
Gulf of
Mexico
CC Palm
VOC 1hr
CC Hillcrest
VOC 24hr
CC Holly
PM2.5
CC West
PM/O3
CC Dona Park
PM/VOC
CC Tuloso
PM/O3
Kingsville
O3/PM
AQSID | Site | PM2.5 | PM10 | VOC
483550025 | CC West Pollution Control | ✓ | — | —
483550026 | CC Tuloso Midway | ✓ | — | —
483550029 | CC Hillcrest | — | — | 24hr
483550032 | CC Dona Park | ✓ | — | 24hr
483550034 | CC Holly Rd | ✓ | — | 24hr
483550083 | CC Palm Ave | — | — | 1hr
482730314 | Kingsville | ✓ | — | —
Volume in Coastal Bend (rows in v0.4.0 pipeline)
PM2.5: ~450k rows across 5 sites (2015–2025 hourly BAM) PM10: sparse — mostly at CC Holly & Dona Park
VOCs:
3.3M rows at CC Palm 1hr AutoGC; 30k rows at CC Hillcrest 24hr AutoGC + Dona Park + Holly
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
6 / 60
Notes: Where our Coastal Bend data lives. Seven AQSIDs matter for Aidan's pollutants: - 483550025 CC West Pollution Control (Nueces): PM2.5 hourly BAM. - 483550026 CC Tuloso Midway (Nueces): PM2.5. - 483550029 CC Hillcrest (Nueces): VOC-only site (24hr AutoGC). - 483550032 CC Dona Park (Nueces): PM2.5 + 24hr VOC. - 483550034 CC Holly Rd (Nueces): PM2.5 + 24hr VOC; heavy industrial. - 483550083 CC Palm Ave (Nueces): the 1hr AutoGC PAMS site — 3.3M VOC rows. - 482730314 Kingsville (Kleberg): PM2.5 + criteria pollutants. Note the DIVISION between hourly PM2.5 BAM sites (real-time continuous) and 24hr filter-based sites — this drives the FRM/FEM comparability question. Note also that PM10 coverage in the Coastal Bend is SPARSE — this will constrain what PM10 analysis we can do.

## Slide 7
SECTION 2
Reference-method foundations
FRM · FEM · AQS parameter codes · method codes · units
Notes: Section 2 — the technical scaffolding everyone needs before we go pollutant-specific. If you only read one section of this deck, read this one. It explains WHY two 'PM2.5' numbers from two different Coastal Bend sites may not be directly comparable, and how to tell in a query whether you're looking at gold-standard filter data or a continuous BAM approximation.

## Slide 8
REFERENCE METHODS
FRM vs FEM — the two federal categories
Every criteria pollutant monitor deployed in the US falls into one of two federal categories.
They are DEFINED by EPA, NOT by the sensor manufacturer, and any change in method category creates a comparability question for our multi-year datasets.
FRM
Federal Reference Method
Defined by 40 CFR Part 50 Appendices
A specific chemistry + hardware combination EPA has designated as THE regulatory yardstick for a pollutant. If EPA disagrees about a compliance value, FRM data wins.
Examples:
PM2.5: gravimetric filter (Appendix L)
PM10: gravimetric filter (Appendix J)
NO2: gas-phase chemiluminescence (Appendix F)
Ozone: UV photometry (Appendix D)
SO2: pulsed fluorescence (Appendix A-1/A-2)
FEM
Federal Equivalent Method
Defined by 40 CFR Part 53
An instrument EPA has individually tested and designated as producing measurements statistically equivalent to the FRM.
FEM lets us have continuous, hourly, near-real-time data that regulatory reporting can still use.
Examples:
PM2.5: Met One BAM 1020/1022, Thermo 5014i, TEOM 1405-FDMS
PM10: BAM 1020, TEOM 1405
Ozone: Teledyne T400, Thermo 49i UV analyzers
NO2 (Class II): Teledyne T500U CAPS spectroscopy
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
8 / 60
Notes: Core distinction. FRM = the definitive federal chemistry-and-hardware combination in 40 CFR Part 50 (mostly filter-based for PM, sits in a lab for weighing; wet chemistry / UV / chemiluminescence for gases). FEM = a specific commercial instrument that EPA has tested and certified as producing statistically equivalent measurements in field conditions, per 40 CFR Part 53. FEMs enable HOURLY data — FRMs typically produce a single 24-hr integrated sample per site per sample day. Neither is inherently 'better' — they measure different things. FRM = compliance-grade truth. FEM = continuous operational data. When someone says 'this site uses FRM,' they mean the site is running a manual filter method whose lab-weighed 24-hr number is the number in the design-value calculation. When someone says 'this site uses FEM,' they mean a continuous automated instrument.

## Slide 9
REFERENCE METHODS
FEM classes — I, II, and III
Class | What it means | PM2.5 examples | How it can drift from FRM
Class I | Manual method 'near-identical' to FRM (different filter model, sampler layout, or brand) | Rupprecht & Patashnick 2025, Andersen sequential FRM equivalents | Minimal — designed as a drop-in for the FRM
Class II | Continuous method with the SAME measurement principle as FRM but automated (e.g., filter-based gravimetric on an automated cycle) | TEOM 1405-DF (dual-channel + FDMS), some BAM designations | Small — automation adds handling artifacts
Class III | Continuous method with a SUBSTANTIALLY DIFFERENT measurement principle from FRM | Met One BAM 1020 (β-attenuation), GRIMM 180 (optical particle counting), Teledyne T640 (light-scattering) | Can drift 10–30% in warm/humid coastal conditions — need field calibration
What this means for our Coastal Bend queries
→ Parameter code 88101 ('PM2.5 – Local Conditions') = FRM + Class I FEM data — the NAAQS-eligible subset. Design values are computed only from 88101.
→ Parameter code 88502 ('Acceptable PM2.5 AQI & Speciation Mass') = Class II/III continuous data (BAM/TEOM). Used for near-real-time AQI reporting but NOT eligible for the annual design value.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
9 / 60
Notes: FEM comes in three flavors. Class I = a manual filter method that behaves essentially like the FRM (same measurement principle, minor hardware differences). Class II = an AUTOMATED filter or filter-equivalent that still measures mass directly. Class III = a COMPLETELY DIFFERENT measurement principle — BAM measures beta-particle attenuation, TEOM measures mass by oscillation frequency, optical instruments measure light scattering. The classification matters because AQS stores Class I under parameter code 88101 (design-value eligible) and Class II/III under 88502 (not eligible). If someone hands you a Coastal Bend PM2.5 annual mean derived from parameter 88502 and claims NAAQS compliance, flag it — that number isn't official.
BAM (Beta Attenuation Monitor) and TEOM (Tapered Element Oscillating Microbalance) are industry-standard, continuous ambient air monitors used to measure the mass concentration of suspended particulate matter (like PM2.5 or PM10) in the air. Both devices report highly accurate, real-time data in micrograms per cubic meter (μ g/m³). [1, 2]
While both instruments physically collect particles from the air, their measurement techniques differ fundamentally: [1]
BAM Technology: The Beta Attenuation Monitor draws air through a specialized filter tape. It uses beta radiation to measure the attenuation (absorption) of beta rays as dust accumulates on the tape. As more particles block the beta particles, the attenuation changes, allowing the device to calculate particulate mass. [1, 2]
TEOM Technology: The Tapered Element Oscillating Microbalance draws air through a filter mounted on the tip of a hollow, oscillating glass tube. As particulate matter collects on the filter, the added weight changes the natural oscillation frequency of the tube. The device measures these exact frequency shifts to continuously calculate the mass of the trapped dust. [1, 2]

## Slide 10
CODES
AQS parameter codes — the pollutant identifier
How the code system works
5-digit integer assigned by EPA that identifies exactly what chemical species is being measured. Different measurement principles for the same species can get different parameter codes. Series prefixes
42xxx — inorganic gases (CO, SO2, NO2, NOx)
43xxx — VOCs: alkanes, alkenes, alkynes, oxygenates
44xxx — photochemical oxidants (Ozone = 44201)
45xxx — aromatic hydrocarbons (BTEX, xylenes)
81xxx–88xxx — particulate matter
88xxx — PM2.5 (mass + speciation)
Master list: aqs.epa.gov/aqsweb/documents/codetables/parameters.html
Code | What it is | In Aidan's pollutants?
81102 | PM10 STP (standard T, P) | PM10
85101 | PM10 – LC (local conditions) | PM10 (uncommon)
88101 | PM2.5 FRM/FEM Local | PM2.5 — canonical
88502 | PM2.5 Acceptable (Class II/III) | PM2.5 — hourly BAM
88500 | PM2.5 Total Atmospheric | PM2.5 (legacy, sparse)
43xxx | Alkanes, alkenes, alkynes, oxygenates (dozens) | VOCs
45xxx | Benzene, toluene, xylenes, TMBs | VOCs (aromatics)
Our v0.4.0 pipeline holds 57 distinct parameter codes across the 51 TCEQ files: 9 criteria + 47 VOCs + 1 sparse PM10 variant. Full list: aq.parameter_reference table on Neon.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
10 / 60
Notes: AQS parameter codes are how EPA (and TCEQ, and our pipeline) uniquely identify what chemical species a row of data measures. 5-digit integers, assigned by EPA, series-prefixed by category. The tricky part is that the same physical species can have multiple parameter codes if it's measured by different methods — this is most acute for PM2.5, where 88101 covers the FRM/Class-I-FEM subset (design-value eligible) while 88502 covers Class II/III continuous data (near-real-time only). Our pipeline preserves the code untouched from TCEQ TAMIS so we can filter on this distinction. For anyone building a query: query aq.parameter_reference first to see the full list of codes we actually hold, along with pollutant_group, chemical family, units, and HAP flag.

## Slide 11
CODES
AQS method codes — the instrument identifier
What a method code encodes
3-digit integer identifying the specific instrument + configuration that produced a row of data. The last 3 digits of an EPA FRM/FEM designation typically become the method code — so EQPM-0798-122 → method 122. Why this matters for us
The method code tells us which instrument was in the shelter that hour. If we don't track it, we can't detect the mid-study sensor change that turned a BAM 1020 into a TEOM 1405, and we'd inadvertently merge two instruments' measurements.
  The TCEQ Annual Monitoring Network Plan documents planned changes each year — but only back to about 2018.
Method | Instrument | Applies to
122 | R&P PM10 hi-vol sampler (legacy TEOM 1400) | PM10 / PM2.5 (legacy)
128 | PE 8700 AutoGC dual-FID (legacy PAMS) | VOCs (older CC Palm)
141 | Hi-vol gravimetric filter (Appendix J) | PM10 24hr — site 0060
142 | PM2.5 filter FRM (Appendix L) | PM2.5 FRM
145 | Met One BAM 1020 | PM2.5 / PM10 continuous
170 | TEOM 1400 (legacy) | PM2.5 (retired)
181 | TEOM 1405-F/FDMS (semi-vol corrected) | PM2.5 continuous
209 | Met One BAM 1020 (newer designation) | PM2.5 / PM10
736 | Met One BAM 1022 (trace-level) | PM2.5 low-conc
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
11 / 60
Notes: Method codes = the layer BELOW parameter codes. Parameter code says WHAT was measured (PM2.5, benzene, ozone); method code says WITH WHICH INSTRUMENT. TCEQ files carry both. The last 3 digits of the EPA FRM/FEM designation typically become the method code — that's the convention. So Met One BAM 1020 designated EQPM-0798-122 shows up as method 122; the same manufacturer's later BAM 1020 designation EQPM-0308-170 becomes method 170 (though that specific number is TEOM in AQS — the convention isn't perfect). Always cross-check the AQS methods HAP list. What we care about: knowing which methods are Class I vs Class III, and detecting when a method code CHANGES mid-record for a single site. That change moment is often a sensor swap that could bias our multi-year time series.

## Slide 12
CODES
Sample duration codes — hourly vs 24-hr
Why this drives table routing
Every raw AQS RD row carries a Sample Duration Code in field 8. This tells us the sampling window that produced the reported value. Our pipeline routes rows to different tables based on this:
1 (hourly) →
aq.pollutant_hourly / vocs_1hr
7 (24hr block) →
aq.pollutant_daily_24hr
X (24hr average) →
aq.pollutant_daily_24hr
In Aidan's pollutants, sample duration matters most for:
PM10 FRM at San Antonio Palo Alto (dur=7)
VOC 24hr canister sampling at CC Hillcrest, Dona Park, Holly (dur=7)
Code | Meaning | Typical usage
1 | 1 hour | Most FEM continuous data
2 | 2 hour | Rare
3 | 4 hour | Some legacy PAMS
5 | 8 hour | Legacy CO
7 | 24-hour block (midnight–midnight) | PM2.5 FRM, PM10 FRM, TO-15 canisters
A | 1 week | Long-integrated HAP samplers
H | 5 min | Special studies
I | 10 min | Special studies
J | 15 min | Some met + gas monitors
P | 30 min | Some met
W | 8-hr rolling (starts at hour) | Ozone 8-hr design values
X | 24-hr average (not block) | Some AutoGC daily
Z | 8-hr rolling (ends at hour) | Alt ozone form
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
12 / 60
Notes: Sample duration codes come from field 8 of the AQS RD Transaction format. Code 1 is our workhorse — most FEM continuous monitors report hourly. Code 7 is the classic 24-hour block from midnight to midnight, used by FRM filter samplers (weighed for the full day) and by canister-based VOC sampling. Codes W and Z are how ozone 8-hour rolling averages get stored — you'll see these downstream when we compute NAAQS design values, though our raw ingest doesn't typically write them (step 03 computes 8-hr max from hourly ozone). Our step_01b routes anything with duration 7 or X to aq.pollutant_daily_24hr instead of pollutant_hourly — that keeps the hourly table conceptually clean (only actual hourly data).

## Slide 13
UNITS
Units — EPA vs TCEQ conventions
Pollutant / class | EPA canonical unit | TCEQ native unit | Our pipeline stores
Ozone (O3) | ppm — parts per million | ppb — parts per billion | ppm (× 0.001 in step 01b)
NO / NO2 / NOx | ppb | ppb | ppb (no conversion)
CO | ppm | ppm | ppm
SO2 | ppb | ppb | ppb
PM2.5 | µg/m³ (LC) | µg/m³ (LC) | µg/m³ (LC)
PM10 | µg/m³ (STP for 81102, LC for 85101) | µg/m³ | µg/m³
VOCs (43xxx, 45xxx) | ppbC — parts per billion Carbon | ppbC | ppbC (no conversion)
Ozone is the ONLY unit conversion in v0.4.0.
step_01b_ingest_tceq_raw.py multiplies parameter 44201 by 0.001 at ingest so downstream code always sees ppm.
ppbC = parts per billion Carbon. For a compound with n carbon atoms:
ppbC = ppbv × n
Standard PAMS reporting convention — normalizes for the O3-forming reactivity of hydrocarbons of different chain length.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
13 / 60
Notes: Units are largely aligned between EPA and TCEQ for our purposes — with one exception: OZONE. TCEQ reports ozone in ppb; EPA's NAAQS is stated in ppm. Our step_01b applies a ×0.001 conversion once, at ingest, so downstream code always works in ppm. For everything else Aidan's working on: PM2.5 and PM10 are in µg/m³ (no conversion), VOCs are in ppbC (Parts Per Billion Carbon — a standard PAMS convention that normalizes hydrocarbons of different chain length to their carbon content, which is the reactive currency in ozone chemistry). If you see a benzene reading of 6 ppbC, that means 6/6 = 1 ppbv (6 carbons in benzene). VOC concentrations in mass units (µg/m³) are computed as ppbv × MW / 24.45 at 25°C — we do NOT apply this conversion in the pipeline; users do it in analysis code when needed.

## Slide 14
INSTRUMENTATION
Sensor evolution over our study window
2015–2025 monitoring landscape for our pollutants
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
TCEQ BAM 1020 dominant
for PM2.5 continuous
TEOM 1400 loses FEM
status (semi-vol bias)
TCEQ Annual Monitoring
Network Plans go public
PM2.5 low-cost sensors
(PurpleAir) proliferate
TEOM 1405-F/FDMS
widely deployed
PM2.5 annual NAAQS
tightened 12→9 µg/m³
Why this matters: if a Coastal Bend PM2.5 site swapped a TEOM 1400 for a BAM 1020 in, say, 2018, the pre- and post-swap concentrations may differ systematically by 10–30% even if true ambient PM2.5 didn't change. TCEQ's Annual Monitoring Network Plan reports document these swaps starting ~2018 but pre-2018 swap history requires a public records request. Method code in our aq.pollutant_hourly is our earliest signal of a transition — flag any (aqsid, parameter_code) pair whose method_code changes mid-record.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
14 / 60
Notes: Timeline of the most consequential sensor / regulation changes over our 2015-2025 window. Most impactful for Aidan's pollutants: (a) the TEOM 1400 losing FEM status around 2018 because of semi-volatile organic aerosol loss in warm climates like the Coastal Bend — many sites transitioned to BAM 1020 or upgraded to TEOM 1405-F with FDMS; (b) the Feb 2024 PM2.5 annual NAAQS tightening from 12 to 9 µg/m³, which changes what our sites look like on the exceedance map (Corpus Christi Holly and Dona Park now exceed the annual standard where they didn't before); (c) low-cost sensors like PurpleAir proliferated 2020+ but they are NOT FEM-eligible and have documented accuracy issues at coastal high-RH conditions — we don't ingest them but users should know the landscape.

## Slide 15
DATA QUALITY
Method-comparability caveats we carry forward
Cross-site comparability
Two Coastal Bend PM2.5 sites running different FEM methods (BAM 1020 vs TEOM 1405-FDMS) will systematically report different means for the SAME ambient PM2.5. Bias 5–15% is typical for the coastal RH range. Report method_code alongside every site-mean.
Mid-record instrument swap
A single AQSID whose method_code changes in, say, 2019 has a step-discontinuity in the time series. Either treat the pre/post segments as separate series, or apply a bias correction based on overlap-period comparison (rarely available in our data).
88101 vs 88502 mixing
aq.pollutant_hourly holds BOTH design-value-eligible (88101) and non-eligible-but-continuous (88502) PM2.5. Filter by parameter_code when computing anything that will be compared to a NAAQS.
24-hr filter vs continuous
Site 480290060 (San Antonio Palo Alto) is 24-hr FRM only (dur=7, routed to aq.pollutant_daily_24hr). Do not join it against hourly sites without collapsing hourly data to daily first.
Coarse fraction (PM10-2.5)
PM10 minus PM2.5 gives the coarse fraction, but only for site-hours where both are co-located AND both use the SAME sample duration. In the Coastal Bend this is rare — plan any coarse-mode analysis accordingly.
VOC 1-hr vs 24-hr AutoGC
CC Palm reports 1-hr AutoGC (nearly continuous). CC Hillcrest, Dona Park, and Holly report 24-hr AutoGC (integrated daily). Compare carefully — the diurnal signal exists in Palm's data but is averaged away in the 24-hr sites.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
15 / 60
Notes: Six caveats to keep in mind for every downstream analysis. These are all surfaced BEFORE we get pollutant-specific so nobody skips them. The biggest three: (1) method-code changes mid-record for a single site (we must audit for these); (2) the 88101 / 88502 split for PM2.5 (design-value calculations must filter to 88101 only); (3) the 1-hr / 24-hr AutoGC distinction for VOCs (aggregation windows are apples-to-oranges if you're not careful). Each pollutant section will re-raise the relevant caveats in context.

## Slide 16
SECTION 3
PM2.5 — fine particulate matter
The most-studied pollutant in air-quality epidemiology. Also the most consequential for our Coastal Bend sites.
Notes: Section 3. PM2.5 is our biggest pollutant by row-count in Coastal Bend and the one with the tightest 2024 regulatory changes. This section covers: what PM2.5 is (chemistry + size), where it comes from, why health effects drove the Feb 2024 NAAQS tightening from 12 to 9 µg/m³, the FRM/FEM landscape (filter vs BAM vs TEOM-FDMS), the 88101 vs 88502 parameter code distinction that matters for design values, weather relationships, and finally what our Coastal Bend sites actually show in 2024.

## Slide 17
PM2.5
What PM2.5 is — size, composition, penetration
Definition (40 CFR Part 50 Appendix L)
Airborne particulate matter with aerodynamic diameter ≤ 2.5 µm — the fraction small enough to penetrate deep into the alveolar region of the lung, where gas exchange occurs. Aerodynamic diameter ≠ physical diameter. It's the diameter of a hypothetical unit-density (1 g/cm³) sphere that has the same terminal settling velocity as the actual particle. This standardizes measurement across irregularly-shaped particles. Not a single species — PM2.5 is a complex mixture of primary and secondary constituents whose composition varies seasonally, geographically, and with source-mix.
Typical Coastal Bend composition (illustrative)
Chart: 
| Sulfate | Organic carbon (OC) | Sea salt | Nitrate | Elemental carbon (EC) | Crustal dust | Ammonium | Trace metals
PM2.5 constituents | 25 | 30 | 12 | 8 | 8 | 10 | 5 | 2
Approximate mass fractions — actual values vary by season, wind sector, and receptor.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
16 / 60
Notes: Grounding definition. Two key concepts: (1) 'aerodynamic diameter' is not the physical size — it's the equivalent unit-density sphere with the same settling velocity, which is what determines respiratory deposition. (2) PM2.5 is a MIXTURE, not a molecule. Sulfate, organic carbon, elemental carbon, nitrate, sea salt, crustal dust, ammonium, and trace metals all contribute. Coastal Bend composition is heavy on organic carbon (from refinery VOC oxidation → SOA), sulfate (SO2 oxidation from refineries + shipping bunker fuel), and sea salt (dominant natural component). This matters because different constituents drive different health effects — sulfate and secondary organic aerosols are more strongly linked to cardiovascular endpoints than crustal dust.

## Slide 18
PM2.5
Sources — primary emissions and secondary formation
Primary anthropogenic
Diesel exhaust (Port of Corpus Christi — 3rd-largest US port by tonnage; heavy diesel trucking on I-37 and SH-358)
Refinery / petrochemical primary emissions (6 major refineries in Nueces County; EC + OC + metals)
Marine bunker fuel combustion (vanadium, nickel — Bozlaker et al. 2013)
Biomass burning (agricultural, especially RGV sugarcane)
Primary natural
Sea salt aerosol from Gulf whitecaps (Na, Cl, Mg, SO4 from DMS oxidation) — dominant baseline in coastal Nueces
Wildfire smoke (episodic — Western US in summer, Central America in spring)
Crustal mineral dust — Saharan trans-Atlantic transport peaks JJA (Prospero et al. 1999, 2014)
Biological particles (pollen, fungal spores)
Secondary formation
Sulfate: SO2 + OH → H2SO4 (gas) + heterogeneous aqueous pathways
Nitrate: NOx → HNO3 → NH4NO3 (largely gas-phase in Coastal Bend heat)
Secondary organic aerosol (SOA) from aromatic + biogenic VOCs — coupled to Coastal Bend refinery-corridor chemistry
Ammonium neutralizes acidic sulfate + nitrate
Coastal Bend transport pathways: SE Gulf flow → sea salt + long-range Saharan dust; sea-breeze convergence recirculates refinery plumes over Hillcrest/Dona Park/Holly; nocturnal land breeze traps emissions at low mixing height along the coast.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
17 / 60
Notes: PM2.5 in the Coastal Bend has three simultaneous source classes. Primary anthropogenic is dominated by the Port of Corpus Christi and the refinery row — diesel exhaust from marine + trucking, plus primary EC/OC and metals from the six major Nueces refineries. Primary natural is dominated by sea salt (baseline year-round) and Saharan dust (June-August). Secondary formation matters more here than most people realize: refinery SO2 → sulfate, NOx → nitrate, and aromatic + olefinic VOCs → SOA. The Ship Channel plume aged over a few hours downwind produces measurable SOA at Hillcrest/Dona Park/Holly. Because of the sea breeze/land breeze cycle, sites near the shore can see dramatic diurnal swings — the sea breeze at 12-3 PM can recirculate morning Ship Channel emissions right back over residential neighborhoods.

## Slide 19
PM2.5 · HEALTH
Health effects — landmark cohort evidence
Study | N | Finding
Six Cities (Dockery et al. 1993, NEJM) | 8,111 adults | 26% mortality gradient across cities differing by ~18 µg/m³ PM2.5
ACS CPS-II (Pope et al. 2002, JAMA) | ~1.2M adults | +4% all-cause mortality per 10 µg/m³ PM2.5; +6% cardiopulmonary; +8% lung cancer
HEI Reanalysis (Krewski et al. 2009) | Extended ACS | Confirmed Pope et al. — robust to confounding adjustment + spatial refinement
Medicare cohort (Di et al. 2017, NEJM) | 60.9M enrollees | Significant mortality below 12 µg/m³ — pivotal evidence for the 2024 NAAQS revision
IARC Monograph 109 (2013) | Meta-analyses | Outdoor air pollution and PM classified Group 1 (known human carcinogen) — lung cancer
GBD 2019 (Murray et al. 2020, Lancet) | Global | ~4.14M deaths and 118M DALYs attributable to ambient PM2.5
Wilker et al. 2023 (BMJ dementia meta) | 16M adults | HR 1.07 (1.04–1.10) per 2 µg/m³ PM2.5 — dementia incidence
→ Effect is monotonic below the previous NAAQS. Di et al. was the specific study Dr. Whitman's team cited when EPA proposed tightening the annual standard to 9 µg/m³ in Feb 2024.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
18 / 60
Notes: PM2.5 health literature is the largest and most consistent body of environmental epidemiology. Chronologically: Dockery 1993 was the landmark small-N study; Pope 2002 scaled to 1.2M adults; Krewski 2009 was the HEI reanalysis that validated the Pope findings under intense scrutiny; Di 2017 used the Medicare cohort (60.9M) and — most importantly for the 2024 NAAQS revision — demonstrated significant mortality effects BELOW the then-current annual standard of 12 µg/m³. That's the study EPA cited most heavily when proposing the tightening to 9 µg/m³. IARC's 2013 classification of outdoor air as Group 1 carcinogen (lung cancer, sufficient evidence) is the standing regulatory-toxicology anchor. GBD 2019 gives the global scale.

## Slide 20
PM2.5 · HEALTH
Health effects — organ systems
Cardiovascular (causal — AHA 2010)
Myocardial infarction, ischemic stroke, heart failure. Mechanisms: autonomic dysregulation, systemic inflammation, endothelial dysfunction, accelerated atherosclerosis. AHA scientific statement (Brook et al. 2010, Circulation 121:2331–2378).
Respiratory + lung cancer
COPD exacerbation, asthma, lower respiratory infections. IARC Monograph 109 (2013) classified outdoor air pollution and PM as Group 1 for lung cancer.
Neurological
Accelerated cognitive decline (Chen et al. 2017, Lancet); dementia meta-analysis (Wilker et al. 2023, BMJ) — HR 1.07 per 2 µg/m³. Mechanism: systemic inflammation + olfactory nerve translocation for UFP.
Prenatal / perinatal (justice-relevant)
Preterm birth: significant association in 79% of studies (19/24); low birth weight in 86% (25/29) — Bekkar et al. 2020 JAMA Netw Open reviewing 32.8M US births. Black mothers and asthmatic populations at highest risk. Direct relevance to Coastal Bend disparities.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
19 / 60
Notes: Four organ-system domains. Cardiovascular has the strongest causal evidence — AHA formally declared causation in 2010. Respiratory + lung cancer is the classical pathway (IARC Group 1 since 2013). Neurological is emerging — 2017 Lancet paper, 2023 BMJ meta-analysis both find dementia incidence increases per µg/m³. Prenatal is especially relevant here: Bekkar 2020 explicitly identified Black mothers and asthmatic populations as high-risk, which maps onto the Hispanic/Latino populations near the Corpus Christi Ship Channel (Hillcrest, Dona Park, Holly) that our sites monitor. This is where the health justice angle sits — even without doing health analysis in this manuscript, it's context to be aware of.

## Slide 21
PM2.5 · REGULATION
NAAQS — the Feb 2024 tightening
Standard | Level | Form
Primary annual | 9.0 µg/m³ | 3-yr avg of annual arithmetic mean (NEW 2024)
Primary 24-hr | 35 µg/m³ | 3-yr avg of 98th percentile of 24-hr values
Secondary annual | 15 µg/m³ | 3-yr avg of annual mean (welfare / visibility)
Secondary 24-hr | 35 µg/m³ | Same as primary
Standard history
1997 — First PM2.5 NAAQS: 65 µg/m³ 24-hr, 15 µg/m³ annual
2006 — 24-hr tightened to 35 µg/m³; annual retained at 15
2012 — Annual tightened to 12 µg/m³
2024 — Annual tightened to 9 µg/m³ (89 FR 16202, effective May 6, 2024), citing Di et al. 2017 evidence of mortality below 12 µg/m³.
WHO 2021 guideline:
5 µg/m³ annual, 15 µg/m³ 24-hr.
2025: EPA announced reconsideration of the 9 µg/m³ standard; 9.0 remains in effect as of mid-2026 pending rulemaking.
EPA-projected 2032 annual benefits of the 2024 revision
up to $46 B
4,500 avoided premature deaths / year
290,000 avoided lost workdays / year
800,000 avoided asthma-symptom days / year
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
20 / 60
Notes: The Feb 2024 tightening from 12 to 9 µg/m³ is the most consequential regulatory change of our study window. It moved multiple South Texas sites — including Corpus Christi Holly (11.61) and Dona Park (10.34) — from attainment to exceedance for the annual standard. Cameron County's Port Isabel (21.02) was already exceeding the old 12 standard but is now far above the new 9. First area designations were scheduled for 2026 with compliance deadlines beginning 2032. Note the WHO guideline is already at 5 µg/m³ — essentially every Coastal Bend site exceeds WHO. Note also EPA in 2025 announced reconsideration of the 9 µg/m³ standard; as of mid-2026 the 9.0 standard remains in effect pending outcome of that rulemaking. If we present this deck to a broader audience, flag that this is a live regulatory moment.

## Slide 22
PM2.5 · METHODS
FRM — the gravimetric filter method (Appendix L)
Filter-based, 24-hr integrated sample
1. 16.67 L/min flow-controlled sampler pulls ambient air through a WINS or VSCC 2.5 µm size-selective inlet. 2. Particulate deposits on a 47 mm Teflon (PTFE) filter over a 24-hour integration period. 3. Filter is equilibrated in the lab at 20–23 °C and 30–40% RH for 24 hours before AND after sampling (controls for hygroscopic mass). 4. Mass difference measured on a microbalance sensitive to ≤ 1 µg. Concentration reported at local ambient conditions. Reference-designated FRM samplers:
BGI PQ200 (Mesa Labs) — most common single-filter FRM
Thermo Partisol 2025i sequential (multi-filter)
R&P Partisol 2025 (legacy)
Strengths
Direct mass measurement — no proxy
The regulatory gold standard — every design value calc uses it
Composition can be analyzed post-hoc (metals, ions, EC/OC)
Immune to hygroscopic humidity bias (controlled equilibration)
Limitations
One 24-hr integrated value per site per sample day (no diurnal)
Manual — filter handling, weighing, transport = costly + slow
Typical sampling cadence: 1-in-3 or 1-in-6 days per EPA schedule
Semi-volatile organic losses can bias low even with FRM
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
21 / 60
Notes: FRM is the compliance-grade truth-teller for PM2.5. Filter-based gravimetric — you pull air through a size-selective inlet, deposit particulate on a Teflon filter, equilibrate it at controlled temperature and humidity, and weigh the filter before and after. Simple, direct, hard to bias. The tradeoffs are that it's SLOW (24-hr integrated) and MANUAL (people go collect filters, drive them to a lab, weigh them). EPA schedules FRM sampling at typically 1-in-3 or 1-in-6 days at each site. That's fine for NAAQS compliance — you don't need diurnal data to compute an annual mean or 98th percentile 24-hr value. But it's insufficient for episode analysis, real-time public warning, or meteorological correlation at hourly scale — which is why FEM continuous methods exist.

## Slide 23
PM2.5 · METHODS
FEM — Beta Attenuation Monitor (BAM 1020)
How a BAM works
1. Ambient air pulled through a size-selective inlet (Sharp Cut Cyclone or PM2.5 impactor) at 16.67 L/min for one hour. 2. Particulate deposits on a glass-fiber filter tape. 3. A carbon-14 (¹⁴C) beta-particle source on one side of the tape and a Geiger-Müller detector on the other measure beta attenuation across the loaded spot. 4. Mass concentration derived from Beer-Lambert attenuation: more particulate = more beta absorption. Reported hourly. TCEQ's continuous PM2.5 workhorse
Met One BAM 1020 became the standard TCEQ CAMS PM2.5 instrument in the early 2010s. Newer BAM 1022 (method code 736) has better precision at low concentrations — relevant given the 9 µg/m³ NAAQS.
EPA FEM designations relevant to Coastal Bend
Instrument | Designation | Method code
BAM 1020 (Met One) | EQPM-0308-170 | 170
BAM 1020 (later) | EQPM-0715-266 | 266
BAM 1020 (early) | EQPM-0798-122 | 122
BAM 1020 (v3) | EQPM-0308-170 | 145 / 209
BAM 1022 (trace) | EQPM-1013-227 | 227 / 736
Note: the LAST 3 DIGITS of the designation typically become the method code in AQS. The same physical instrument can carry multiple designations if EPA re-tested it against a new NAAQS review.
BAM in high-humidity coastal air
Sea-salt aerosol growth at RH > 70% can inflate hourly BAM readings by ~10-15% relative to co-located FRM. Correction typically applied at TCEQ level.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
22 / 60
Notes: BAM 1020 is our workhorse for hourly PM2.5 in Coastal Bend. The physics: particulate deposits on a filter tape, a C-14 beta source on one side and a Geiger detector on the other measure how much the loaded spot attenuates beta particles — more particulate = more attenuation. Beer-Lambert converts that to mass concentration. TCEQ adopted BAM 1020 across CAMS in the early 2010s replacing the failed TEOM 1400. The important nuance in Corpus Christi is that high humidity + sea-salt aerosol causes hygroscopic growth that can inflate BAM readings 10-15% relative to what a co-located gravimetric FRM would report. TCEQ applies a correction at the CAMS level; users of aq.pollutant_hourly are seeing the corrected values. Method codes 122, 145, 170, 209, 227, 266, and 736 all point to some BAM 1020/1022 configuration.

## Slide 24
PM2.5 · METHODS
FEM alternatives — TEOM-FDMS and optical
TEOM 1405-F with FDMS
Tapered Element Oscillating Microbalance
Principle:
Particulate deposits on a filter mounted on the tip of an oscillating tapered element. As mass loads, resonant frequency shifts — mass computed from Δf. Why the FDMS retrofit? The original 1400ab TEOM heated its inlet to reduce water bias — but this also volatilized ammonium nitrate and semi-volatile organics, producing systematic 10–30% negative bias in warm climates. EPA withdrew 1400ab FEM designation ~2018. The FDMS (Filter Dynamics Measurement System) uses an alternating dry / diffusion-dryer denuder configuration to capture semi-volatile losses. FEM designation EQPM-0609-181 → method code 181. Tradeoff: ~3× the capital cost of a BAM 1020. Deployment is budget-limited at TCEQ.
Optical + low-cost
Optical particle spectrometers (FEM)
GRIMM EDM 180: laser scattering, size-resolved, EQPM-0311-195
→ method code 195. Class II FEM.
Thermo 5030 SHARP: combined nephelometer + BAM in one box for cross-validation.
Low-cost sensors (NOT FEM)
PurpleAir, Clarity Node-S, AirNow-Tech: laser scattering at ~$200-$500 per node.
Documented
positive bias at high RH
— problematic in Corpus Christi's chronic 70-80% RH.
Not eligible for regulatory NAAQS design values.
Useful for high spatial density but require correction (EPA publishes a PurpleAir correction equation for NAAQS-adjacent reporting).
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
23 / 60
Notes: Two FEM alternatives worth knowing for Coastal Bend. TEOM 1405-F with FDMS is the top-tier continuous FEM — it directly addresses the semi-volatile organic aerosol loss problem that killed the older TEOM 1400. But it's expensive (~3× BAM cost), so TCEQ has selectively deployed it. Optical particle spectrometers (GRIMM, Thermo SHARP) are the third path — size-resolved by laser scattering, Class II FEM. Low-cost sensors (PurpleAir etc.) have proliferated since 2018 but are NOT FEM. For Corpus Christi specifically, PurpleAir data should be viewed with extra caution because of the chronic high humidity — the sensor's positive bias is worst exactly in the meteorological regime we operate in. If we want to use citizen-science PurpleAir data for supplementary spatial coverage, we'd need to apply EPA's PurpleAir correction equation.

## Slide 25
PM2.5 · CODES
88101 vs 88502
 | 88101 – Local Conditions | 88502 – Acceptable AQI/Speciation
What it stores | FRM filter data + Class I FEM data + validated regulatory continuous FEM (BAM/TEOM under regulatory validation) | Non-regulatory continuous data (BAM, TEOM, optical) intended for near-real-time AQI reporting
NAAQS design value? | YES — the ONLY source for annual mean + 24-hr 98th-percentile design values | NO — used for AQI + episode monitoring, not compliance calculations
Time resolution | 24-hr integrated (FRM) or 1-hr (validated continuous) | Typically 1-hr
Coastal Bend example | CC West, Kingsville filter-based FRM (dur=7); validated BAM data at CC Holly | Non-validated BAM/TEOM hourly at some CAMS sites
QUERY RULE: For any NAAQS-comparable analysis, filter WHERE parameter_code = 88101. For general trend/episode/weather-correlation work, use both — but always retain parameter_code as a covariate so you can subset.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
24 / 60
Notes: This one slide is the single most important operational takeaway for anyone querying aq.pollutant_hourly for PM2.5. Parameter code 88101 = 'PM2.5 Local Conditions' = the design-value-eligible subset. Includes FRM filter data (24-hr integrated) and any continuous FEM data that TCEQ has validated for regulatory use. Parameter code 88502 = 'Acceptable PM2.5 AQI and Speciation Mass' = continuous BAM/TEOM data intended for near-real-time AQI but NOT eligible for design value calculation. If someone gives you a 'PM2.5 annual mean' derived from 88502 data and claims NAAQS compliance, it's technically not — the official design value is what compliance is measured against, and that comes from 88101 only. Our pipeline holds both codes in aq.pollutant_hourly. Filter accordingly. This is the failure mode Aidan flagged in the last team meeting — we can't publish PM2.5 numbers without knowing which code they came from.

## Slide 26
PM2.5 · CODES
PM2.5 method codes in Coastal Bend data
Method | Instrument | Class | Notes for our data
141 | Hi-vol gravimetric filter (Appendix J) | FRM (PM10) | Not PM2.5 but flagged: appears at site 480290060 (Palo Alto) which is 24hr-only
142 | Partisol / BGI PQ200 filter (Appendix L) | FRM | The gold-standard PM2.5 FRM — validated 24-hr filter
145 | Met One BAM 1020 continuous | Class III FEM | Common TCEQ CAMS PM2.5 continuous; ~2010-mid-2010s
170 | TEOM 1400 (legacy, retired ~2018) | Class III FEM (retired) | Watch for step-change if a site transitions off 170
181 | TEOM 1405-F with FDMS | Class III FEM | Semi-vol corrected; ~3× cost of BAM; selective deployment
195 | GRIMM EDM 180 optical | Class II FEM | Less common in TCEQ Coastal Bend deployments
209 | Met One BAM 1020 (later designation) | Class III FEM | Newer CAMS deployments (Met One EQPM-0308-170)
227 | Met One BAM 1022 (trace-level) | Class III FEM | Improved precision at low concentrations — post-2015
266 | Met One BAM 1020 (v3 designation) | Class III FEM | Later revision
736 | Met One BAM 1022 | Class III FEM | Standardized TCEQ code for BAM 1022
Method-code diagnostic: SELECT aqsid, MIN(date_local), MAX(date_local), method_code FROM aq.pollutant_hourly WHERE pollutant_group='PM2.5' GROUP BY aqsid, method_code ORDER BY aqsid; — any AQSID with more than one method_code has had a sensor change.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
25 / 60
Notes: Ten method codes we're likely to encounter for PM2.5. The critical ones: 142 = filter FRM (compliance-grade); 145/209/266 = BAM 1020 continuous; 181 = TEOM-FDMS (semi-vol corrected); 227/736 = BAM 1022 (trace). Method 170 flags a legacy TEOM 1400 — if you see this in a site's history and then it disappears around 2018, that's likely the FEM-designation withdrawal event and the site probably swapped to a BAM. Method 141 is hi-vol PM10 (Appendix J) — it appears in our data at site 480290060 Palo Alto which is a 24-hr-only PM10 site (routed to aq.pollutant_daily_24hr, not the hourly table). The diagnostic query at the bottom of the slide is the quickest way to identify AQSIDs with mid-record sensor changes.

## Slide 27
PM2.5 · TIMELINE
PM2.5 sensor evolution at TCEQ CAMS 2010–2025
Coastal Bend PM2.5 instrumentation transitions
2010
2012
2014
2016
2018
2020
2022
2024
2025
TCEQ pilot BAM 1020
deployments
BAM 1020 becomes
TCEQ CAMS standard
BAM 1022 begins
rollout (trace-level)
EPA withdraws TEOM 1400
FEM designation (semi-vol)
TEOM 1405-F/FDMS
selective deployment
Low-cost sensor networks
proliferate in Corpus
PM2.5 NAAQS
tightened 12 → 9 µg/m³
Action: Query aq.pollutant_hourly for PM2.5 method_code transitions at each of our 5 Coastal Bend PM2.5 sites. Any transition through code 170 → 145/209 needs to be documented in our methods writeup and considered as a potential step change in the time series.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
26 / 60
Notes: The full PM2.5 sensor story for our 2010-2025 window. Three transitions matter most for our Coastal Bend sites: (1) The BAM 1020 rollout ~2013 — this affected ALL CAMS sites. Pre-2013 continuous data may be TEOM 1400. (2) The TEOM 1400 FEM-designation withdrawal in 2018 — any site still on 1400 at that point had to swap or its data lost regulatory value. (3) The BAM 1022 upgrades starting 2015-ish (method 227/736) — these have better precision at low concentrations and matter more now that the annual NAAQS is 9 µg/m³ (small biases matter more when the threshold is lower). We should query our data to find the specific transition dates at each of our 5 Coastal Bend PM2.5 sites and document them in the methods section.

## Slide 28
PM2.5 · WEATHER
PM2.5 – weather relationships (peer-reviewed)
Wind speed
Higher winds dilute local emissions but transport marine sea salt AND long-range Saharan dust. Coastal Bend's ESE 5-10 m/s brings cleaner marine air; strong easterly waves (summer) bring dust.
Wind direction (biggest signal)
Single most important variable for Coastal Bend source attribution. Ship Channel wind rose points at Hillcrest/Dona Park/Holly; ESE = Saharan dust chemistry (Si, Al, Fe, Ca).
Boundary layer height
Nocturnal stable BL (100–300 m winter) traps emissions → morning peaks. Convective daytime BL (1500–2500 m summer) dilutes. Sea breeze creates internal structure → fumigation peaks inland.
Temperature
Net effect complex: higher T accelerates SOA formation but shifts NH4NO3 to gas phase and enhances mixing. Dawson 2007, Tai 2010.
Humidity (RH)
Sulfate/nitrate/ammonium undergo hygroscopic growth at RH > 70%. Inflates optical + BAM readings in chronic 74–78% RH of Corpus Christi. FRM controls via 30-40% RH equilibration.
Sea-breeze cycle
Dominant mesoscale feature in Coastal Bend. Daily onshore front concentrates emissions at the leading edge → short, high-conc PM2.5 pulses at inland receptor sites. Ignore this and source attribution goes wrong.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
27 / 60
Notes: Weather explains up to 50% of daily PM2.5 variance across the US per Tai et al. 2010 — this is the standard reference for weather-PM regression. For the Coastal Bend specifically, the sea-breeze/land-breeze cycle is the dominant mesoscale forcing and it MUST be resolved in any analysis. Wind direction is our single strongest source-attribution lever — conditional bivariate probability functions (CBPF) at CC Hillcrest/Dona Park/Holly should show characteristic rose alignments with the Ship Channel bearing during industrial episodes and ESE alignment during Saharan events. Humidity is a measurement-artifact issue — BAM and optical readings inflate at high RH from sea-salt hygroscopic growth. FRM controls this via 30-40% RH lab equilibration; continuous FEM data in Corpus's chronic 74-78% RH needs careful interpretation.

## Slide 29
PM2.5 · OUR DATA
Coastal Bend PM2.5 — 2024 in our pipeline
Site (AQSID) | County | 2024 annual mean | vs 9 µg/m³ | 2024 24-hr 98p | vs 35 µg/m³
Port Isabel (480612004) | Cameron | 21.02 µg/m³ | EXCEEDS | 64.96 µg/m³ | EXCEEDS
Corpus Christi Holly (483550034) | Nueces | 11.61 µg/m³ | EXCEEDS | 39.67 µg/m³ | EXCEEDS
Corpus Christi Dona Park (483550032) | Nueces | 10.34 µg/m³ | EXCEEDS | n/a in 2024 | —
Brownsville Roca (480611098) | Cameron | n/a | — | 36.56 µg/m³ | EXCEEDS
Corpus Christi West (483550025) | Nueces | < 9 µg/m³ | — | < 35 µg/m³ | —
Corpus Christi Tuloso (483550026) | Nueces | < 9 µg/m³ | — | < 35 µg/m³ | —
Kingsville (482730314) | Kleberg | < 9 µg/m³ | — | < 35 µg/m³ | —
Reading these numbers: Port Isabel's 21 µg/m³ annual is extreme — investigate for a very localized source, a dust-dominated regime, or a sensor issue before publishing. Corpus Christi Holly's 11.61 exceeding the new 9 µg/m³ standard is the most population-consequential finding — residential neighborhood adjacent to the Ship Channel, historically Hispanic/Latino, aligns with the Bekkar 2020 environmental-justice risk profile. Dona Park is a similar story at 10.34. Follow-up: site-specific method_code audit for all three, review 3-yr rolling average (design value is 3-yr avg, not single-year), confirm 88101 vs 88502 subset used.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
28 / 60
Notes: This is where the deck lands on actual data. Three sites in our region exceed the new 9 µg/m³ annual standard for 2024 alone: Port Isabel (Cameron; 21 µg/m³ — extreme, needs investigation), Corpus Christi Holly (Nueces; 11.61 — the most consequential for population exposure), and Corpus Christi Dona Park (Nueces; 10.34). Two sites exceed the 24-hr 98th percentile: Port Isabel and CC Holly with Brownsville Roca at 36.56 also over 35. The important interpretive move: NAAQS compliance is judged on a 3-YEAR ROLLING AVERAGE, not a single year, so a single-year exceedance is not automatically a violation. We need to compute 3-yr rolling design values before making compliance claims. And critically — verify these values were computed from parameter code 88101 only, not from 88502. This is exactly the type of analysis that should live in Aidan's manuscript.

## Slide 30
SECTION 4
PM10 — coarse particulate matter
Thoracic-fraction mass. In the Coastal Bend, dominated by sea salt + episodic Saharan dust.
Notes: Section 4. PM10 in the Coastal Bend has SPARSE coverage compared to PM2.5 — that's a genuine data-availability limitation. But it stays scientifically important because (a) sea salt is a first-order coarse source that PM2.5 misses, (b) Saharan dust events deliver biological + metal cargo with documented health effects, (c) recurrent La Niña + drought increases local dust generation. This section is shorter than PM2.5 by design — reflects both the data and the science.

## Slide 31
PM10
What PM10 is — the thoracic fraction
Definition (40 CFR Part 50 Appendix J)
Airborne particulate matter with aerodynamic diameter ≤ 10 µm — often called the thoracic fraction because these particles penetrate past the larynx. PM10 is not a single population — it's the sum of two overlapping modes:
Fine mode (≤ 2.5 µm) = PM2.5 (secondary aerosol, combustion)
Coarse mode (2.5–10 µm) = mechanical + biological (crustal dust, sea salt, pollen)
Coarse-mode chemistry differs sharply from PM2.5:
Crustal: Al, Si, Ca, Fe, K (wind-blown dust)
Sea salt: Na, Cl, Mg, sulfate (bubble-bursting → Coastal Bend baseline)
Biological: pollen, spores, endotoxin, bacteria
Respiratory deposition by size
Nose / pharynx
PM10 (2.5–10 µm)
Mucociliary clearance; upper-airway inflammation
Trachea / bronchi
PM10-2.5 mixed
COPD, asthma exacerbation, bronchial irritation
Alveoli / systemic
PM2.5 fine + UFP
Cardiovascular, systemic inflammation, deep-lung retention
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
30 / 60
Notes: PM10 is defined by aerodynamic diameter ≤ 10 µm — the fraction small enough to pass the larynx and reach the thoracic region. Critically, PM10 CONTAINS PM2.5 within it: the coarse mode is PM10-minus-PM2.5, roughly 2.5-10 µm. Chemistry of the coarse mode is very different from PM2.5 — mostly primary and mechanically-generated: crustal (Al/Si/Ca/Fe from wind-blown dust), sea salt (Na/Cl/Mg from Gulf whitecaps), and biological (pollen, fungal spores, bacteria). The deposition diagram on the right shows why size matters: PM10 deposits mostly in upper airways (nose, throat, upper bronchi) where mucociliary clearance operates; PM2.5 penetrates to alveoli where systemic inflammation and cardiovascular pathways activate. This drives different regulatory approaches (24-hr PM10 vs annual PM2.5) and different epidemiological signals.

## Slide 32
PM10 · SOURCES
PM10 sources — dominant in the Coastal Bend
Sea salt aerosol
Generated by bubble bursting and jet drop production in whitecaps. Dominant coarse-mode source in coastal environments. Coastal Bend's prevailing SE Gulf wind delivers near-continuous sea salt. Studies in Mediterranean and Gulf coasts show > 50% of summer PM10 mass at coastal receptors can be sea salt.
Windblown mineral dust
Emission scales roughly as u*³ above threshold friction velocity (~5-7 m/s at 10 m for undisturbed soils). Local dust from South Texas agricultural belt (grain sorghum, cotton, corn). Multi-year La Niña drought (2020-2025) has increased soil erodibility and dust event frequency.
Trans-Atlantic Saharan dust
June-August peak; Bozlaker et al. 2019 quantified an 85% dust increase in Houston/Galveston PM10 during the July 2008 Saharan intrusion. The same air mass reaches Coastal Bend. Signal is biological + mineral — carries endotoxin, fungal spores, respirable metals (Bozlaker 2024 ES&T).
Road dust (paved + unpaved)
Resuspended by vehicle turbulence. Paved-road fraction dominates urban PM10 in Corpus Christi's Ship Channel corridor. Unpaved-road dust more relevant to rural Kleberg / San Patricio / Jim Wells.
Port + Ship Channel fugitive dust
Port of Corpus Christi is the largest US crude oil export port. Bulk material handling (petroleum coke, aggregate, fertilizer), unpaved industrial yards, and heavy diesel traffic generate localized coarse PM around Hillcrest/Dona Park/Holly.
Sea-salt derived chemistry
Aging sea salt reacts with anthropogenic sulfate and nitrate to produce HCl, ClNO2, and other reactive halogens — a secondary coarse-mode chemistry pathway that adds to the primary sea-salt signal.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
31 / 60
Notes: PM10 in the Coastal Bend has three dominant classes: (1) sea salt — the year-round baseline, driven by prevailing SE Gulf winds. Bubble bursting in whitecaps produces droplets that evaporate to leave salt particles in the coarse mode. (2) Windblown dust — locally from agricultural belts (sorghum, cotton, corn) and increasingly from drought-induced soil exposure; long-range from the Sahara during June-August. (3) Anthropogenic fugitive — the Port of Corpus Christi (largest US crude oil export port) is a major bulk-materials handler and diesel-traffic hub with associated coarse-PM emissions along the Ship Channel corridor. All three are simultaneously active. Wind direction is the diagnostic tool — ESE = marine + Saharan; NW/N = agricultural/urban; ENE = industrial.

## Slide 33
PM10 · EPISODES
Saharan dust — the biggest episodic driver
Trans-Atlantic transport
Prospero & Lamb (2003, Science): Barbados-measured African dust 1965-1998 was strongly anti-correlated with Sahelian rainfall — drying → dust. Yu et al. (2015, RSE): CALIPSO lidar quantified the Sahara exports ~182 million tons of dust per year over its western edge; ~132 Mt reaches the Atlantic; a fraction reaches the Gulf of Mexico. Peak Coastal Bend impact
June–August
— coincident with maximum African easterly wave activity and the mature Saharan Air Layer.
Multi-day pulses
— a single Saharan intrusion event can double a coastal site's daily PM10 for 2-4 days.
Biological + metal cargo (Bozlaker 2024 ES&T): the June 2020 "Godzilla" dust plume carried respirable metals, bacteria, and fungi across Houston — the same air mass reached Corpus.
Health signal
Ortiz-Martínez et al. (2015, Mediators of Inflammation): in Puerto Rico, pediatric asthma claims tracked average PM10, PM10 increment, and African Dust Event days. Mechanism: inhaled endotoxin + fungal β-glucans → TLR-4 / TLR-2 airway inflammation → asthma exacerbation. Directly transferable to Gulf Coast during summer Saharan intrusions.
Coupled hurricane suppression
Prospero & Mayol-Bracero (2013, BAMS): Saharan dust suppresses tropical cyclogenesis through three mechanisms — SAL dry-air entrainment, dust radiative cooling of Main Development Region SSTs, and mid-level trade wind inversion strengthening. Net: heavy dust weeks REDUCE local hurricane risk while SIMULTANEOUSLY delivering a health-relevant PM10 burden. This coupling matters for climate-attribution analyses of PM10 trends.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
32 / 60
Notes: Saharan dust deserves its own slide because it's the single largest episodic driver of PM10 in the Coastal Bend, and because it's meteorologically coupled to hurricane suppression in a way that makes the trend analysis interesting. Peak season is June-August, driven by African easterly wave activity and the Saharan Air Layer. Multi-day pulses can double daily PM10 at coastal sites. Bozlaker's group has quantified the Houston contribution and its biological cargo. Ortiz-Martínez showed the health signal in Puerto Rico (endotoxin → asthma exacerbation) which is mechanistically portable to the Gulf Coast. Prospero & Mayol-Bracero (2013) documented the hurricane suppression coupling — heavy dust weeks reduce cyclogenesis. This means dust-heavy years may show lower hurricane frequency AND higher PM10 simultaneously — a joint climate variable, not two independent ones.

## Slide 34
PM10 · HEALTH
PM10 health effects — coarse-fraction distinct pathway
Respiratory hospital admissions
Adar et al. (2014) systematic review: PM10-2.5 (coarse) associations with respiratory hospital admissions are 'as strong or stronger than for PM2.5' — survives publication-bias adjustment. Asthma and COPD endpoints most consistent.
Cardiovascular (weaker signal than PM2.5)
AHA 2010 statement (Brook et al., Circulation 121:2331–2378): evidence for PM10-2.5 cardiovascular effect is 'suggestive' rather than causal. Malig & Ostro (2009) found California associations concentrated in Hispanic populations.
Biological cargo — dust + asthma
Ortiz-Martínez et al. (2015) Puerto Rico pediatric asthma tied to African Dust Event days. Bozlaker (2024) documented respirable metals, bacteria, fungi in Houston Saharan dust — Gulf Coast exposure is analogous.
Windborne fungi — Valley Fever + Aspergillus
Tong et al. (2017, GRL): PM10 links to Valley Fever timing in Arizona. Coccidioidomycosis rare in Coastal Bend, but the mechanism (windborne spore transport in coarse fraction) is analogous to Aspergillus / Alternaria during local dust events.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
33 / 60
Notes: PM10 health effects are DISTINCT from PM2.5's — not just a diluted version. Coarse-fraction toxicology centers on upper-airway inflammation, mucociliary irritation, and biological cargo delivery. The Adar 2014 systematic review is the key coarse-PM epidemiology reference — coarse-PM respiratory associations are as strong as (or stronger than) PM2.5 in that dataset. Cardiovascular signal is weaker than PM2.5 (AHA 2010 said 'suggestive' not causal). The distinctive PM10 health story is BIOLOGICAL CARGO — endotoxin, fungal β-glucans, bacteria delivered by dust events (Ortiz-Martínez 2015, Bozlaker 2024). Even if we don't do health analysis in this manuscript, the story matters for framing why PM10 is worth studying alongside PM2.5 even with our sparse coverage.

## Slide 35
PM10 · REGULATION
PM10 NAAQS — one standard remains, one was revoked
Current standard
150 µg/m³
24-hour primary + secondary
Statistical form: not to be exceeded more than once per year on average over three consecutive years
What was REVOKED
Annual 50 µg/m³ standard (1987 → 2006)
EPA's 2006 rationale (upheld by the D.C. Circuit): 1. Epidemiological evidence for chronic effects of coarse PM (as distinct from PM2.5) was weak; 2. PM10 as an indicator was 'poorly matched' to the coarse fraction because it also included PM2.5. The annual PM2.5 standard covers chronic fine-particle exposure; the retained 24-hr PM10 standard covers episodic thoracic coarse exposures.
The 'once per year on average' form + Exceptional Events Rule
The 1-exceedance-per-year statistical form is important for the Coastal Bend. Coastal + arid regions experience natural transient PM10 exceedances during dust storms, hurricanes, and windblown episodes. EPA's Exceptional Events Rule (40 CFR 50.14) allows states to petition to exclude natural-event exceedances from regulatory determinations. Texas has historically flagged Saharan dust intrusions under this provision — meaning even a single-year > 150 µg/m³ dust event in Corpus doesn't automatically drive a violation.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
34 / 60
Notes: Two facts about PM10 NAAQS. First: only the 24-hr standard remains (150 µg/m³, not to be exceeded more than once per year on average over 3 years). Second: the annual 50 µg/m³ standard was REVOKED in 2006, and EPA's reasoning was that (a) chronic PM10-only effects — as distinct from PM2.5 within PM10 — were epidemiologically weak, and (b) PM10 as an indicator is a poor match to the true coarse fraction. So chronic PM regulation moved to PM2.5, and PM10 stayed as an episodic-event standard. The Exceptional Events Rule matters here: Texas has used it to exclude Saharan dust intrusion exceedances from regulatory determinations. So a single 200 µg/m³ 24-hr value in Corpus during a Godzilla plume doesn't automatically create a violation — TCEQ can petition EPA to exclude it as an exceptional event.

## Slide 36
PM10 · METHODS
PM10 measurement — FRM + FEM
FRM (Appendix J)
24-hr integrated sample on a filter through a 10-µm size-selective inlet. Gravimetric mass determination at STP (25 °C, 1 atm). Reference samplers:
Andersen SA-2000 (hi-vol)
Wedding & Associates PM10 hi-vol
BGI PQ200 (small vol, low-flow)
Thermo Partisol 2025i sequential
Graseby GMW-321
Appendix O also defines a PM10-2.5 (coarse fraction) reference method using PAIRED dichotomous FRMs as a subtraction.
Continuous FEM (hourly)
Met One BAM 1020
First PM10 FEM designation 1998 (63 FR 41253; EQPM-0798-122). Same physics as the PM2.5 BAM — β-attenuation through loaded filter tape — but with a 10-µm cyclone inlet instead of 2.5-µm.
Thermo/R&P TEOM 1400ab / 1405
Mass by frequency shift of an oscillating tapered element. Semi-volatile loss less severe for coarse mode than for PM2.5 (coarse aerosol is drier and less volatile), so TEOM PM10 designations survived even where PM2.5 TEOM was withdrawn.
Optical (GRIMM, Thermo 5030 SHARP)
Size-resolved by laser scattering. Cover PM10 + PM2.5 + PM1 in a single instrument.
Low-cost sensors: NOT suitable for PM10.
PurpleAir and similar underestimate coarse fraction — sensor optical response saturates below ~1 µm. Kaur & Kelly 2023 (AMT): 5-6× underestimation during dust events. Do not substitute.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
35 / 60
Notes: PM10 measurement mirrors PM2.5 with a few key differences. FRM is 40 CFR Part 50 Appendix J — 24-hr gravimetric filter through a 10-µm size-selective inlet, mass reported at STP (25°C, 1 atm — this is different from PM2.5 which is reported at local conditions). Hi-vol samplers like Wedding, Andersen SA-2000, and Graseby GMW-321 are the classical hardware. Continuous FEM options are BAM 1020 (same physics as PM2.5 BAM, different inlet), TEOM 1400/1405 (frequency-shift; importantly, the semi-volatile loss issue that killed PM2.5 TEOM designations is much smaller for PM10 because coarse aerosol is less volatile), and optical spectrometers (GRIMM, Thermo SHARP). Low-cost sensors are essentially useless for PM10 — Kaur & Kelly 2023 documented 5-6× underestimation during dust events, which is exactly when you'd want to use PurpleAir for supplementary coverage.

## Slide 37
PM10 · CODES
PM10 codes in our Coastal Bend data
Parameter codes
Code | Name | In our data?
81102 | PM10 Total 0-10um STP | YES — dominant
85101 | PM10 - LC (local conditions) | sparse
86101 | PM10-2.5 coarse (derived) | very sparse — needs paired PM10 + PM2.5
Method codes we see
Method | Instrument | Note
141 | Hi-vol Appendix J FRM | 24-hr filter — Palo Alto site 0060
145 | Met One BAM 1020 continuous | Typical TCEQ CAMS
149 | Met One BAM 1020 variant | Alternate inlet config
209 | Met One BAM 1020 (later desig) | Post-2015 TCEQ deployments
122 | TEOM legacy (R&P) | Largely phased out
Units: µg/m³ — but WATCH the temperature reference
AQS unit code 001 = µg/m³ at STP (25°C, 1 atm) — corresponds to parameter code 81102 (the dominant PM10 code) AQS unit code 105 = µg/m³ at LC (local ambient) — corresponds to parameter code 85101 For a hot near-sea-level Coastal Bend site, STP vs LC differ by only a few percent (a 30°C ambient temperature reduces air density by ~1.7% relative to STP). Non-negligible at high altitude or in extreme heat, but small in our region. In our pipeline, most Coastal Bend PM10 rows are STP-referenced.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
36 / 60
Notes: For PM10, three parameter codes and five method codes matter for our data. Parameter 81102 (PM10 STP) is the dominant one — it's what the 24-hr NAAQS is judged against. 85101 (PM10 LC) is less common. 86101 is the derived PM10-2.5 coarse fraction — only computable where paired PM10 and PM2.5 exist, which in the Coastal Bend is rare enough that coarse-mode analysis will be spatially patchy. Method codes: 141 is the hi-vol FRM (24-hr filter); 145 and 209 are BAM 1020 continuous; 149 is a BAM variant; 122 is legacy TEOM. Units note: PM10 at STP vs LC is a small difference (~1.7%) at Coastal Bend elevations but should be tracked in metadata for reproducibility.

## Slide 38
PM10 · WEATHER
PM10 – weather relationships
Wind speed (STRONG positive)
Emission rate scales as u*³ above threshold friction velocity (~5-7 m/s at 10 m). High-wind episodes (fronts, dryline) generate largest local PM10 excursions. Below cloud, wind also drives sea-spray production.
Wind direction
Coastal Bend split: SE (marine) → sea salt aerosol; N/NW (continental) → agricultural + rangeland dust. Direction-resolved source apportionment is essential.
Precipitation (STRONG negative)
Wet deposition scavenging: PM10 typically drops 40–80% during and after rain. Below-cloud impaction is highly efficient for coarse particles (inertial impaction). Rain events reset the PM10 baseline.
Relative humidity
Hygroscopic growth of sea salt at RH > 70% inflates effective particle size + speeds settling. For Coastal Bend's chronic 74-78% RH: sea salt shortens residence time BUT inflates optical readings.
ENSO (La Niña → dust)
La Niña winters in South Texas → below-normal precipitation → drier soils → more dust generation. The 2020-2025 Southern Plains drought (consecutive La Niña years, NOAA 2025) drove both increased local dust and reduced wet-deposition losses.
Hurricane season (coupling)
Saharan dust suppresses Atlantic cyclogenesis via SAL dry-air entrainment, dust radiative cooling of MDR SSTs, and inversion strengthening. Coastal Bend simultaneously experiences dust burden AND reduced local hurricane risk in dust-heavy summers.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
37 / 60
Notes: PM10 has stronger and more mechanistically interpretable meteorological dependencies than PM2.5. Wind speed is critical (u*³ scaling for wind-blown dust; also drives sea spray). Wind direction gives source attribution. Precipitation strongly scavenges via below-cloud impaction — coarse particles are highly efficient scavengers. RH matters through sea-salt hygroscopic growth. Two large-scale climate modes: ENSO (La Niña → South Texas drought → dust) and Saharan-dust/hurricane coupling (heavy dust years suppress cyclogenesis AND deliver PM burden). The 2020-2025 Southern Plains drought under consecutive La Niña years is documented in the NOAA 2025 assessment — this drove recent PM10 dust events in Texas.

## Slide 39
PM10 · OUR DATA
Coastal Bend PM10 — sparse coverage, but still important
What's in our v0.4.0 pipeline
Total PM10 rows: ~87,990 (across all 13 South Texas counties)
Coastal Bend PM10 sites: candidates include CC Holly (483550034) and CC Dona Park (483550032) — needs explicit pipeline audit before writeup.
24-hr FRM site outside Coastal Bend: 480290060 San Antonio Palo Alto (Bexar) — 636 filter rows in aq.pollutant_daily_24hr; routed separately from hourly BAM data.
2024 NAAQS exceedances (150 µg/m³ 24-hr):
NONE in our data. Consistent with historical Coastal Bend behavior — sea salt + background dust rarely push above 100 µg/m³ absent a Saharan intrusion or local dust event.
Why PM10 still matters for our study
1. Sea salt is a first-order coarse-mode source that PM2.5 measurement misses. Any Coastal Bend aerosol characterization that ignores coarse fraction is incomplete.
2. Episodic Saharan dust delivers biological + metal cargo with documented respiratory-inflammatory consequences (Ortiz-Martínez 2015, Bozlaker 2024).
3. Local drought + agricultural dust events are increasing under recurrent La Niña forcing.
4. Port + Ship Channel fugitive dust is a local exposure with environmental-justice implications that a PM2.5-only network cannot resolve.
→ Recommendation: emphasize both the coverage limitation and the scientific importance. Advocate for expanded coarse-fraction monitoring rather than treating PM10 as a legacy metric.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
38 / 60
Notes: Wrapping the PM10 section. Two important takeaways: (1) Coastal Bend PM10 coverage is genuinely sparse — TCEQ has historically prioritized PM2.5, ozone, and VOCs over PM10 in this region. Our ~87,990 total PM10 rows are spread across the state; Coastal Bend candidates are CC Holly and CC Dona Park (needs audit) plus the 24-hr Palo Alto FRM (outside Coastal Bend). No 2024 NAAQS exceedances, consistent with background behavior. (2) But PM10 remains scientifically important in the Coastal Bend for four reasons: sea salt (missed by PM2.5), Saharan dust with biological cargo, La Niña-driven local dust, and port fugitive dust with environmental-justice implications. Our recommendation for the manuscript framing: acknowledge the coverage limitation, but argue for its retention and expansion — don't treat PM10 as a legacy metric to be dropped.

## Slide 40
SECTION 5
VOCs — volatile organic compounds
Ozone + PM precursors. HAPs on the criteria menu. PAMS network. AutoGC + TO-15 canisters.
Notes: Section 5. VOCs are the most complex pollutant class in our data — no single NAAQS, 47 distinct chemical species in our pipeline, two different sampling paradigms (continuous AutoGC vs 24-hr canister), and multiple regulatory frameworks (HAP §112(b), PAMS, TCEQ ESL). The Coastal Bend has 3.3M rows at just one site — CC Palm — plus smaller 24-hr datasets at Hillcrest, Dona Park, and Holly.

## Slide 41
VOCS
What VOCs are — regulatory + chemical definition
The regulatory definition (40 CFR §51.100(s))
"Any compound of carbon, excluding CO, CO2, carbonic acid, metallic carbides or carbonates, and ammonium carbonate, which participates in atmospheric photochemical reactions..." In practice: carbon-containing gases + vapors that (a) exist in gas phase at ambient T and (b) contribute to ozone/SOA formation through OH-radical oxidation. EPA-exempt species (NOT VOCs for regulatory purposes even though they contain carbon):
Methane (43201) — very slow OH reaction
Ethane (43202) — low reactivity — EXEMPT since 2005
Acetone (43551), several HFCs, and others
Our pipeline preserves
all 43xxx + 45xxx species that TCEQ measures — regulatory exemption status doesn't affect what we ingest.
Why we track VOCs
Ozone precursors
OH + VOC → RO2 → NO2 → hν → O3. The photochemical engine of summer smog. Speciated VOC data is required for photochemical modeling (CAMx, CMAQ).
SOA precursors
Aromatic + biogenic VOCs oxidize to secondary organic aerosol — a major PM2.5 constituent in the Coastal Bend refinery corridor.
Direct HAP exposure
10 of our 47 species are Hazardous Air Pollutants (CAA §112(b)). Benzene alone is a Group 1 human carcinogen.
Source fingerprinting
Ratios (e.g., benzene/toluene) identify source classes — mobile, refinery, biogenic, unconventional O&G. Critical for attribution.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
39 / 60
Notes: VOCs are defined by EPA as carbon-containing compounds that participate in atmospheric photochemistry — with explicit exemptions for CO, CO2, methane, and a growing list of low-reactivity species (ethane exempted 2005, followed by acetone, HFCs, etc.). The regulatory definition matters for state SIP-VOC accounting but NOT for our pipeline — we ingest every 43xxx and 45xxx species TCEQ measures. Four reasons to track VOCs: they're the primary ozone precursors alongside NOx (which Jasmine handles); they oxidize to secondary organic aerosol (linking to Aidan's PM2.5 work); several are direct-exposure HAPs (benzene = Group 1 human carcinogen); and the speciation lets us fingerprint sources (benzene/toluene ratio distinguishes mobile from refinery emissions).

## Slide 42
VOCS
Chemical families in our data — 47 species
Breakdown
21
Paraffins (alkanes, C₂–C₁₁)
species
4
Cycloalkanes
species
12
Olefins (alkenes/dienes/alkynes)
species
11
Aromatics (BTEX + TMBs)
species
Family | Example species | Codes
Paraffins | Ethane, Propane, n-Butane, Isobutane, n-Pentane, Isopentane, n-Hexane, n-Heptane, n-Octane, … | 43202-43291, 43954, 43960
Cycloalkanes | Cyclopentane, Cyclohexane, Methylcyclopentane, Methylcyclohexane | 43242, 43248, 43261, 43262
Olefins | Ethylene, Propylene, 1-Butene, cis/trans-2-Butene, 1,3-Butadiene, Isoprene, Acetylene | 43203-43206, 43216-43228, 43243, 43280
Aromatics | Benzene, Toluene, Ethylbenzene, m/p-Xylene, o-Xylene, 1,2,4-TMB, 1,3,5-TMB, Styrene, Cumene | 45109, 45201-45225
10 HAPs (CAA §112(b)): Benzene, Toluene, Ethylbenzene, m/p-Xylene, o-Xylene, Isopropylbenzene (Cumene), Styrene, 1,3-Butadiene, n-Hexane, 2,2,4-Trimethylpentane. Benzene, 1,3-Butadiene = IARC Group 1.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
40 / 60
Notes: The 47 VOC species in our pipeline sort into four chemical families. PARAFFINS (alkanes) are the largest — 21 species from ethane through n-undecane and 2-methylheptane. These are combustion + fugitive fuel vapor. CYCLOALKANES are the smallest family (4 species) but important in refinery signatures. OLEFINS (alkenes, dienes, alkynes) include the very-reactive 1,3-butadiene (HAP + Group 1 carcinogen) and biogenic isoprene (dominant natural source). AROMATICS include BTEX (benzene/toluene/ethylbenzene/xylenes — all HAPs) plus trimethylbenzenes, styrene, and cumene. Ten of the 47 species are HAPs under CAA §112(b); benzene and 1,3-butadiene are IARC Group 1 human carcinogens. The parameter reference table in aq.parameter_reference has the is_hap flag pre-computed.

## Slide 43
VOCS · HEALTH
VOC health effects — the BTEX + 1,3-butadiene axis
Benzene (45201) — Group 1 carcinogen
IARC Group 1 (known human carcinogen). Causes acute myeloid leukemia in occupational cohorts. EPA IRIS inhalation unit risk = 7.8×10⁻⁶ per µg/m³; inhalation RfC = 30 µg/m³. TCEQ ESL: long-term 4.5 µg/m³ (1.4 ppb annual).
1,3-Butadiene (43218) — Group 1 carcinogen
IARC Group 1 (2008). Hematolymphatic cancer. EPA IRIS IUR = 3×10⁻⁵ per µg/m³ — nearly 4× more potent than benzene per unit mass. Inhalation RfC = 2 µg/m³ (~0.9 ppb). Formerly APWL-listed in Houston Milby Park.
Toluene, Xylenes (BTEX)
Toluene (45202) — HAP; CNS depressant at occupational exposure. TCEQ long-term ESL ~330 ppb. Xylenes (45109 m/p; 45204 o) — HAPs; irritation + CNS effects. IARC Group 3 for toluene, xylenes (not classifiable — insufficient evidence).
n-Hexane (43231) neurotoxicity
HAP under §112(b). Occupational chronic exposure causes peripheral neuropathy via 2,5-hexanedione metabolite. Not IARC-classified for cancer. Concentration in ambient air typically far below occupational thresholds.
Formaldehyde + carbonyls
Not currently in Aidan's dataset (parameter code 43502) — TCEQ AutoGC networks don't always report — but noted here because PAMS Type 2 sites ARE required to sample every 3 hours per 40 CFR 58 App. D §5(b). Formaldehyde = Group 1 carcinogen.
Chronic community exposure
The EPA National Air Toxics Assessment (NATA) uses ambient VOC concentrations to compute cancer + non-cancer risk. TCEQ's Air Pollutant Watch List (APWL) tracks areas with persistent elevated ambient toxics.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
41 / 60
Notes: VOC health effects are compound-specific. The two biggest concerns for ambient exposure are benzene (Group 1 carcinogen; acute myeloid leukemia) and 1,3-butadiene (Group 1; hematolymphatic cancer). Butadiene is nearly 4× more potent per unit mass. BTEX collectively (benzene, toluene, ethylbenzene, xylenes) are the workhorse industrial air toxics — all HAPs, all measured by AutoGC in the Coastal Bend at CC Palm. n-Hexane is a HAP but for neurotoxicity (peripheral neuropathy) rather than cancer; ambient levels are typically well below occupational thresholds. TCEQ's Effects Screening Levels are the state-level toxicological benchmarks (short-term 1-hr + long-term annual). Ambient carbonyls (formaldehyde etc.) aren't in our current TCEQ pull — noting them because they're required at PAMS Type 2 sites and formaldehyde is Group 1.

## Slide 44
VOCS · REGULATION
HAPs — the Clean Air Act §112(b) framework
§112(b) Hazardous Air Pollutants
Established by Clean Air Act Amendments of 1990. Original list = 189 pollutants. Current = 188 HAPs after selective delistings (caprolactam 1996, MEK 2005, EGBE 2004). Regulated via NESHAPs — National Emission Standards for HAPs (40 CFR Part 63) — which impose MACT (Maximum Achievable Control Technology) standards on 174+ source categories. Relevant NESHAP subparts for Coastal Bend:
Subpart CC & UUU — Petroleum Refineries (benzene, toluene, xylenes, 1,3-butadiene). 2015 amendments added
fenceline benzene monitoring
(action level 9 µg/m³ annual avg).
Subpart R & BBBBBB — Gasoline Distribution.
Subpart U — Group I Polymers & Resins (1,3-butadiene, styrene).
Species | IARC | IRIS class
Benzene | Group 1 | Known human carcinogen
1,3-Butadiene | Group 1 | Carcinogenic to humans
Ethylbenzene | Group 2B | Under reassessment
Isopropylbenzene | Group 2B | Likely human carcinogen
Styrene | Group 2A | Reasonably anticipated
Toluene | Group 3 | Not classifiable
Xylenes (m/p/o) | Group 3 | Not classifiable
n-Hexane | — | Neurotoxicant, not carcinogen
2,2,4-Trimethylpentane | — | No IRIS cancer assessment
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
42 / 60
Notes: The Clean Air Act §112(b) HAP framework — 188 pollutants regulated by MACT standards under NESHAPs in 40 CFR Part 63. Two big Coastal Bend relevances: (1) Subpart CC and UUU — Petroleum Refineries — the 2015 amendments introduced FENCELINE BENZENE MONITORING with an action level of 9 µg/m³ annual average. This is why Corpus Christi refineries have benzene monitors along their perimeter fences. If a fenceline monitor exceeds action level, the refinery has to take corrective action. (2) Subpart U covers polymers and resins production (butadiene, styrene). Our 10 HAPs sort into three tiers: Group 1 (benzene, butadiene — definitively carcinogenic), Group 2A/2B (ethylbenzene, isopropylbenzene, styrene — probably or possibly), and Group 3 (toluene, xylenes — insufficient evidence). n-Hexane and 2,2,4-TMP are HAPs for reasons other than cancer (neurotoxicity, generic tox).

## Slide 45
VOCS · REGULATION
Regulatory framework — no NAAQS, but plenty of oversight
Federal
No NAAQS for VOCs as a class (unlike criteria pollutants)
Ozone NAAQS 0.070 ppm regulates VOC + NOx as ozone precursors
PM2.5 NAAQS 9 µg/m³ captures SOA from VOCs indirectly
§112(b) HAPs regulated by NESHAP MACT standards
EPA IRIS assessments provide toxicity values (IUR, RfC)
Texas (TCEQ)
Effects Screening Levels (ESLs) — permit + ambient benchmarks, NOT enforceable NAAQS
Short-term ESL (1-hr) = acute + odor + acute vegetation
Long-term ESL (annual) = chronic health + vegetation
Air Pollutant Watch List (APWL) tracks areas with persistent elevated toxics
Development Support Documents (DSDs) publish per-chemical derivations
Mobile-source
Mobile Source Air Toxics Rules (MSAT1 2001, MSAT2 2007)
MSAT2: gasoline benzene ≤ 0.62 vol% annual avg (from 2011)
MSAT2 is the dominant driver of declining urban ambient benzene
Mobile sources = ~50–60% of ambient benzene exposure nationally
Onboard refueling vapor recovery (Stage II) — TX participates
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
43 / 60
Notes: VOCs sit in a regulatory space very different from criteria pollutants — NO NAAQS applies to VOCs as a class, but they're regulated three different ways. Federal: (a) indirectly via the ozone NAAQS (VOC + NOx are the O3 precursors), (b) indirectly via PM2.5 NAAQS (SOA from VOCs), (c) directly via NESHAP MACT for HAPs. Texas: TCEQ publishes Effects Screening Levels (ESLs) — screening benchmarks used in permitting and ambient review, but NOT enforceable standards. Short-term ESL = 1-hr acute; long-term = annual chronic. Air Pollutant Watch List flags areas with persistent elevated toxics. Mobile-source: MSAT2 rule capped gasoline benzene at 0.62 vol% annual avg from 2011 — this is why urban ambient benzene has been declining. Mobile sources historically account for 50-60% of ambient benzene exposure nationally.

## Slide 46
VOCS · PROGRAM
PAMS — the Photochemical Assessment Monitoring Stations network
Statutory origin + purpose
Established by Section 182(c)(1) of the Clean Air Act (1990 CAAA). Requires enhanced monitoring in serious, severe, or extreme ozone nonattainment areas. 2015 NAAQS revision
expanded the PAMS network. Post-2015 requirement: any NCore site in a CBSA ≥ 1,000,000 population must collect PAMS measurements. Enhanced Monitoring Plan (EMP)
must be submitted to EPA Regional Administrator within 2 years of any Moderate-or-above ozone nonattainment designation. Ozone season = June, July, August (minimum). Many sites operate year-round.
Required PAMS measurements
40 CFR Part 58 Appendix D §5(b)
Hourly speciated VOCs (57-compound target list)
3 carbonyl samples/day (formaldehyde, acetaldehyde, acetone) on 1-in-3 day schedule
Hourly O3
Hourly NO, true NO2, and total reactive nitrogen (NOy)
Surface meteorology (T, wind, RH, P, precip, mixing height, solar radiation)
Upper-air met at the EMP-designated enhanced site
Site types (Type 1-4)
Type 1: upwind/background · Type 2: max precursor impact · Type 3: max ozone · Type 4: extreme downwind
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
44 / 60
Notes: PAMS is the federal enhanced-monitoring backbone for ozone nonattainment areas. Established by CAA §182(c)(1) in 1990, expanded in the 2015 NAAQS revision. Nonattainment-triggered — Serious, Severe, or Extreme classifications require it. Post-2015: any NCore site in a CBSA ≥ 1M population must collect PAMS. San Antonio is Serious nonattainment (bumped 2024). Corpus Christi is currently Attainment, so PAMS is not federally required there — BUT TCEQ operates AutoGC sites in Corpus voluntarily (CC Palm is our data source), which is the origin of our 3.3M-row 1-hr VOC dataset. Required measurements include hourly speciated VOCs (the 57-compound PAMS target list), carbonyls every 3 hours at Type 2 sites, hourly O3 + NO + true NO2 + NOy, and full surface meteorology. Site types classify by function: background, max precursor impact, max ozone, downwind.

## Slide 47
VOCS · METHODS
AutoGC — how continuous hourly VOC data happens
Automated Gas Chromatograph workflow
1. Ambient air sampled every hour (typical 200–700 mL). 2. Preconcentration via Peltier-cooled multi-stage sorbent trap (Tenax, Carbopack, Carbosieve) at -10 to -30 °C. Water managed via Nafion membrane dryer or Kori-xr cold trap. 3. Ballistic heating (300–380 °C) desorbs analytes into GC carrier gas. 4. Dual-column separation: Al2O3/KCl PLOT (C2–C5) + DB-1 non-polar (C6–C12 aromatics), Deans-switched. 5. Detection: dual FID (carbon response → ppbC) or MS for confirmation. 6. Data pushed to LIMS → TAMIS → EPA AQS. Cycle time: 20–60 min. Cryogen-free (Peltier) or LN₂-cooled.
Commercial systems in deployment
System | Notes
Markes TT24-7 / UNITY-CIA | Cryogen-free TD; U.S. PAMS reference
Synspec GC955-611/811 | Turnkey; dual-instrument C2-C12
Chromatotec airmoVOC C2-C12 | Dual-FID; lowest MDLs (~1-10 ppt)
PerkinElmer Clarus + TDx | Legacy PAMS platform
Entech 7200A + Agilent GCMS | Cryogenic; TO-15A overlap
Calibration + reporting
57-component PAMS gas standards (Restek/Airgas P/N 26370, Linde P/N 34445, Apel-Riemer custom) at 20-60 ppbC. Daily auto-cal; 5-7 point curves quarterly. Internal standards: BCM, 1,4-DFB, chlorobenzene-d5.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
45 / 60
Notes: AutoGC is the technology behind our 3.3M-row 1-hr VOC dataset at CC Palm and the county-level VOC files. The workflow: sample ambient air every hour, preconcentrate on a Peltier-cooled sorbent trap, ballistic-heat to desorb, separate on a dual-column GC (alumina PLOT for light hydrocarbons + non-polar DB-1 for heavier aromatics), detect with dual flame ionization detectors (FID gives carbon response — this is why results are reported in ppbC not ppbv). Cycle time 20-60 min. Commercial systems: Markes TT24-7 (US PAMS reference), Synspec GC955 (EU-common turnkey), Chromatotec airmoVOC (dual-FID, lowest detection limits), PerkinElmer Clarus (legacy), Entech+Agilent (cryogenic, GC-MS confirmation). Calibrated against 57-component PAMS gas standards. TCEQ standardized on some subset of these; the specific system at CC Palm should be documented in TCEQ's Annual Monitoring Network Plans.

## Slide 48
VOCS · METHODS
EPA Method TO-15 — the canister method
Attribute | TO-15 (1999) | TO-15A (2019)
Working range | Soil vapor + ambient (200-500 pptv reporting) | Ambient focus (20 pptv reporting)
Canister cleanliness | < 200 pptv per analyte | < 20 pptv per analyte
Calibration ceiling | ~50 ppbv | ~5 ppbv (better low-level linearity)
MDL (benzene, toluene) | 0.1–0.5 ppbv | 5–15 pptv
30-day stability test | Not required | Required, at 40-50% RH
Gauges | Analog OK | Digital/certified, 0.1 PSI resolution
Programs using TO-15
NATTS — National Air Toxics Trends Stations (27 sites)
UATMP — Urban Air Toxics Monitoring Program
PAMS ozone-precursor sites (canister confirmation of AutoGC)
State networks: TCEQ, CARB, NYSDEC
Vapor intrusion (ITRC / ASTM E2600)
Canister types: SUMMA-passivated (NiCrOx layer, standard); Silonite (silica CVD, more inert). Sizes 0.4-15 L. 6L canisters = de facto standard for 24-hr integrated NATTS samples. Coastal Bend relevance: our 24-hr AutoGC data at CC Hillcrest, Dona Park, Holly is effectively equivalent to TO-15 canister methodology in reporting cadence — 1-in-6 day sampling is typical.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
46 / 60
Notes: TO-15 is the EPA canister-based GC/MS method for ambient VOCs. Two versions matter: the original 1999 TO-15 (EPA/625/R-96/010b) covered ~65-70 HAPs at 200-500 pptv reporting limits, suitable for soil vapor and moderate ambient. The 2019 TO-15A tightened the reporting limit 10× (to 20 pptv), reduced the calibration ceiling to focus on low-level linearity, and added a 30-day canister stability test. TO-15A MDLs for benzene and toluene are ~5-15 pptv. Canisters are SUMMA-passivated stainless steel (standard) or Silonite (more inert). 6L canisters are the NATTS standard for 24-hr integrated samples. Programs using TO-15: NATTS (27 sites nationwide), UATMP, PAMS confirmation, state networks. For our Coastal Bend data: the 24-hr AutoGC at CC Hillcrest, Dona Park, and Holly serves a similar temporal cadence to TO-15 canister sampling.

## Slide 49
VOCS · CODES
VOC parameter codes — 43xxx and 45xxx series
Code series
43xxx
Alkanes, alkenes, alkynes, oxygenates (aldehydes / ketones)
45xxx
Aromatic hydrocarbons (BTEX, xylenes, styrene, trimethylbenzenes)
43000 (special)
Sum of PAMS target compounds — a QC summary field
43102
Total NMOC — non-methane organic compound (bulk sum via TO-12)
Master list: aqs.epa.gov/aqsweb/documents/codetables/parameters.html
Code | Species | Family | HAP?
43202 | Ethane | Paraffin | no (exempt)
43203 | Ethylene | Olefin | no
43206 | Acetylene | Alkyne | no
43212 | n-Butane | Paraffin | no
43218 | 1,3-Butadiene | Olefin | YES (Group 1)
43220 | n-Pentane | Paraffin | no
43231 | n-Hexane | Paraffin | YES
43243 | Isoprene | Olefin | no (biogenic)
43248 | Cyclohexane | Cycloalkane | no
43250 | 2,2,4-Trimethylpentane | Paraffin | YES
45109 | m/p-Xylene | Aromatic | YES
45201 | Benzene | Aromatic | YES (Group 1)
45202 | Toluene | Aromatic | YES
45203 | Ethylbenzene | Aromatic | YES
45204 | o-Xylene | Aromatic | YES
45220 | Styrene | Aromatic | YES
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
47 / 60
Notes: The AQS parameter code series for VOCs are 43xxx (alkanes, alkenes, alkynes, oxygenates) and 45xxx (aromatics). Special code 43000 is a computed sum of PAMS target compounds; 43102 is total NMOC (bulk sum via TO-12 cryogenic method — not per-species). The table on the right shows a representative sample from our data with HAP flags. Note key species: 45201 = Benzene (Group 1 carcinogen), 43218 = 1,3-Butadiene (Group 1), 43231 = n-Hexane (HAP for neurotoxicity), 43250 = 2,2,4-TMP (isooctane, HAP). Isoprene 43243 is biogenic (dominant natural source, from vegetation) — always visible in summer daytime data. 43202 ethane is regulatory-exempt but we still measure it. Full 57-species list lives in aq.parameter_reference on Neon with is_hap and chemical_family columns pre-computed.

## Slide 50
VOCS · CODES
VOC method codes — AutoGC + canister families
Method | Instrument / method | Class | Typical use
122 | 6L ambient canister, dual-FID (PAMS) | Canister | 24-hr integrated samples
123 | 6L pressurized canister, dual-FID (PAMS) | Canister | 24-hr integrated
128 | PerkinElmer 8700 AutoGC subambient dual-FID | AutoGC | Hourly, PAMS-target only
142 | Preconcentration/thermal desorber AutoGC (PE Clarus) | AutoGC | Continuous PAMS
146 | PE 8700 AutoGC, 6L pressurized canister | Hybrid | Combined workflow
101 | Canister subambient, multi-detector GC | Canister | Multi-detector confirmation
109 | SS canister subambient, GC/MS (TO-15) | TO-15 | HAP confirmation
110 | SS canister pressurized, GC/MS (TO-15) | TO-15 | HAP confirmation
127 | 6L subambient SS canister, GC/MS (TO-15) | TO-15 | NATTS reference
129 | 6L pressurized SS canister, GC/MS (TO-15) | TO-15 | NATTS reference
Diagnostic for our Coastal Bend data: CC Palm's 3.3M rows are AutoGC (methods 128 or 142); CC Hillcrest / Dona Park / Holly 24-hr rows are canister-based (methods 122/123 or TO-15 family 127/129).
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
48 / 60
Notes: VOC method codes break into three categories. AutoGC methods (128, 142, 146) = continuous hourly PAMS-style; these are what generate our 3.3M-row CC Palm dataset. Canister PAMS methods (122, 123) = 6-L canister 24-hr integrated samples analyzed by dual-FID; these are what our 24-hr sites (CC Hillcrest, Dona Park, Holly) most likely use. TO-15 GC/MS methods (109, 110, 127, 129) = canister samples analyzed by mass spectrometry for HAP confirmation — the NATTS reference standard. Query aq.pollutant_hourly (or the vocs_1hr and vocs_24hr tables) with method_code to disambiguate.

## Slide 51
VOCS · UNITS
Units — ppbC + why VOCs are reported that way
What ppbC means
ppbC = parts per billion CARBON
For a molecule with n carbon atoms: ppbC = ppbv × n
Examples:
Benzene (C6H6): 1 ppbv = 6 ppbC
Toluene (C7H8): 1 ppbv = 7 ppbC
Ethane (C2H6): 1 ppbv = 2 ppbC
Why carbon-normalize?
Ozone-formation potential scales roughly with reactive carbon count, not with mole count. A 10 ppbv toluene contributes about 10× more ozone-forming carbon than 1 ppbv toluene. Reporting in ppbC lets you compare across species of different chain length for photochemical modeling.
Converting between units
Species | Formula | C# | 1 ppbv →
Benzene | C6H6 | 6 | 6 ppbC ≈ 3.19 µg/m³
Toluene | C7H8 | 7 | 7 ppbC ≈ 3.77 µg/m³
Ethylbenzene | C8H10 | 8 | 8 ppbC ≈ 4.34 µg/m³
m/p-Xylene | C8H10 | 8 | 8 ppbC ≈ 4.34 µg/m³
1,3-Butadiene | C4H6 | 4 | 4 ppbC ≈ 2.21 µg/m³
Ethane | C2H6 | 2 | 2 ppbC ≈ 1.23 µg/m³
n-Hexane | C6H14 | 6 | 6 ppbC ≈ 3.52 µg/m³
µg/m³ conversion at 25 °C, 1 atm: µg/m³ = ppbv × MW / 24.45
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
49 / 60
Notes: VOC units confusion is one of the most common analysis pitfalls. TCEQ TAMIS and EPA AQS both report VOCs in ppbC (parts per billion Carbon) — NOT ppbv (parts per billion volume). To convert: divide by carbon count of the molecule. A benzene reading of 6 ppbC = 1 ppbv (benzene has 6 carbons). A toluene reading of 7 ppbC = 1 ppbv. This convention exists because ozone-formation potential scales roughly with reactive carbon count, so ppbC gives a natural comparison across species of different chain length in photochemical modeling. For MASS units (µg/m³): µg/m³ = ppbv × MW / 24.45 at 25°C, 1 atm. The conversion table on the right shows worked examples for the key HAPs. Users doing health-risk analysis typically want µg/m³ so they can compare to EPA IRIS RfC values — that requires converting ppbC → ppbv → µg/m³.

## Slide 52
VOCS · SOURCES
Coastal Bend VOC sources — Ship Channel + Eagle Ford proximity
Corpus Christi Ship Channel refineries
Six major refineries in Nueces County (Citgo East + West, Flint Hills East + West, Valero, CC Refining) release fugitive BTEX + olefins + paraffins. Fenceline benzene monitors (per 2015 NESHAP Subpart CC) provide independent QC on VOC emissions.
Port of Corpus Christi
Largest US crude oil export port. Bulk transfer of petroleum + condensate; marine tanker loading vapor losses; diesel bunker combustion. VOC signature is complex — mixed crude, refined products, condensate all pass through.
Eagle Ford Shale proximity
Nueces isn't in Eagle Ford proper but is DOWNWIND of Karnes / Wilson / Atascosa production. Long-range VOC transport from flaring, compressor stations, and diesel fleets contributes background hydrocarbon load.
Mobile sources
I-37, US 77, US 181 diesel + gasoline VOC emissions. Mobile-source benzene is roughly 50-60% of national ambient benzene per EPA — declining under MSAT2 (0.62 vol% gasoline benzene cap since 2011).
Biogenic isoprene + monoterpenes
South Texas forests, brush, and agricultural vegetation emit large amounts of isoprene in summer daytime (temperature + light driven). Isoprene 43243 dominates ambient VOC totals during midday, especially at background sites.
Trans-boundary + marine
Cross-Gulf transport can carry biomass burning VOCs from Mexican agricultural fires. Marine sources contribute DMS-derived sulfate (precursor to secondary aerosol) but negligible primary VOC.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
50 / 60
Notes: Coastal Bend VOC sources cluster in three geographic regions. In Nueces County immediately: (a) the Corpus Christi Ship Channel refinery corridor — six major refineries with associated fugitive BTEX emissions, fenceline benzene monitoring per 2015 NESHAP CC + UUU amendments (9 µg/m³ action level); (b) the Port of Corpus Christi — largest US crude oil export port with associated tanker loading vapor + diesel bunker emissions. Regional: (c) Eagle Ford Shale — Karnes, Wilson, Atascosa are the production counties; Nueces is downwind. Ubiquitous: mobile sources (diesel + gasoline along I-37, US 77, US 181; declining under MSAT2). Natural: isoprene from vegetation dominates midday summer VOC totals at background sites — this is why any anthropogenic-source-attribution analysis must separate biogenic from anthropogenic signal (typically via the isoprene time series or a chemical mass balance).

## Slide 53
VOCS · OUR DATA
Coastal Bend VOCs in our v0.4.0 pipeline
Site (AQSID) | County | Sampling | Rows | Notes
CC Palm Ave (483550083) | Nueces | 1-hr AutoGC | ~3.3 M | PAMS-target hourly; the workhorse dataset
CC Hillcrest (483550029) | Nueces | 24-hr canister | ~30 k | Ship Channel-adjacent
CC Dona Park (483550032) | Nueces | 24-hr canister | ~30 k | Residential + industrial
CC Holly Rd (483550034) | Nueces | 24-hr canister | ~30 k | Historically Hispanic residential
County-level Nueces VOC files | Nueces | Various | aggregated | TCEQ region-wide roll-up
The 1-hr / 24-hr apples-to-oranges caveat
CC Palm's 1-hr AutoGC captures diurnal variation (morning rush hour peaks, midday isoprene surges, refinery plume events). 24-hr sites average that away — comparing means or medians directly is misleading.
Analytical opportunity: source fingerprinting
The rich speciation at CC Palm supports source apportionment via PMF or CMB. Signature ratios: benzene/toluene (mobile vs refinery), isoprene fraction (biogenic marker), i-pentane/n-pentane (fuel evaporation), C2H2/CO (combustion age).
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
51 / 60
Notes: This is what our Coastal Bend VOC dataset actually looks like. CC Palm dominates by volume: 3.3M rows of 1-hr AutoGC. The three 24-hr sites (Hillcrest, Dona Park, Holly) contribute ~30k rows each. The 24-hr sites are geographically closer to the Ship Channel residential exposure zone. Two operational reminders: (1) don't compare 1-hr Palm means directly to 24-hr Hillcrest means — different sampling windows produce different-looking distributions because Palm sees the diurnal peaks and Hillcrest averages them out. (2) The rich speciation at CC Palm is a genuine analytical asset — with 47 species hourly for a decade, we can do PMF source apportionment, ratio diagnostics (benzene/toluene ratios distinguish mobile from refinery signatures; isoprene fraction identifies biogenic contribution), and cluster analysis on wind-direction-conditioned VOC profiles.

## Slide 54
VOCS · WEATHER
VOC – weather + diurnal relationships
Temperature — dual effect
Higher T increases biogenic isoprene emissions (exponentially) AND evaporative fuel losses. Also accelerates OH oxidation, shortening VOC lifetime — net diurnal minimum at midday, peak in early morning.
Wind direction (critical)
CC Palm's ESE sector = Ship Channel plume; NW = urban Corpus; NE = trans-Karnes-Eagle-Ford. Conditional bivariate probability functions (CBPF) on VOC species by wind sector = source-attribution workhorse.
Boundary layer height
Nocturnal shallow BL traps VOCs → morning peaks. Daytime convective BL (1500–2500 m) dilutes. Sea breeze creates internal structure that can produce localized plume enhancement inland.
Photolysis + OH reactivity
Solar-driven OH radical concentration peaks midday. Reactive VOCs (alkenes, aromatics) show characteristic midday minima; unreactive species (ethane, propane) don't. Ratio of reactive to unreactive → aged vs fresh emission signature.
Humidity
High RH accelerates heterogeneous aqueous-phase oxidation, particularly for aldehydes and other polar VOCs. Less critical than for particulate but relevant for SOA formation from VOC precursors.
Sea-breeze cycle
As with PM2.5, dominant mesoscale feature. Morning offshore land breeze carries Ship Channel VOCs offshore; afternoon onshore sea breeze recirculates them back over Corpus. This drives the characteristic double-peak diurnal at some sites.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
52 / 60
Notes: VOC diurnal behavior in the Coastal Bend is driven by six mechanisms interacting: (1) temperature — increases biogenic isoprene emissions exponentially AND evaporative fuel losses AND OH reaction rates. Nonlinear net effect: usually a midday reactive-VOC minimum and early-morning peak. (2) Wind direction — the strongest source-attribution lever. CBPF plots at CC Palm by chemical species should reveal Ship Channel, urban, and Eagle Ford transport signatures. (3) Boundary layer height — nocturnal trapping → morning VOC peaks; daytime dilution. (4) OH reactivity — reactive species (butadiene, aromatics) show midday minima; unreactive (ethane) don't. Ratio gives photochemical age. (5) Humidity — matters for aqueous-phase oxidation of polar VOCs. (6) Sea-breeze cycle — critical mesoscale modulator; morning offshore, afternoon onshore, can produce double-peak diurnals at recirculation sites.

## Slide 55
SECTION 6
Synthesis & references
Cross-pollutant comparison · Aidan's next steps · Bibliography
Notes: Section 6. Cross-pollutant table for at-a-glance comparison; concrete next-step tasks for our own work; then the peer-reviewed bibliography and contact page.

## Slide 56
SYNTHESIS
Cross-pollutant comparison — at a glance
Dimension | PM2.5 | PM10 | VOCs
Dominant sources | Refinery + diesel + secondary (SO4/NO3/SOA) + sea salt | Sea salt + Saharan dust + fugitive | Refineries + mobile + biogenic + Eagle Ford
NAAQS | 9 µg/m³ ann (2024) + 35 µg/m³ 24-hr p98 | 150 µg/m³ 24-hr (annual REVOKED 2006) | None as a class; HAP-specific via NESHAP
FRM chemistry | Gravimetric filter (App. L) | Gravimetric filter (App. J) | Canister GC/MS (TO-15 / TO-15A)
Dominant FEM | BAM 1020, TEOM 1405-FDMS | BAM 1020 | AutoGC (dual-FID PAMS)
AQS parameter codes | 88101 (design-value), 88502 (continuous) | 81102 (STP), 85101 (LC) | 43xxx + 45xxx (57 species)
Units in our pipeline | µg/m³ LC | µg/m³ STP | ppbC
Coastal Bend rows | ~450k (5 sites hourly) | sparse — 4 sites + Palo Alto 24-hr | ~3.4M (Palm + 3× 24-hr)
2024 exceedances | Holly + Dona Park + Port Isabel (annual) | None | Fenceline benzene monitoring active
Health signal | Cardiovascular + respiratory + neuro + prenatal | Respiratory + biological cargo | Benzene + 1,3-butadiene cancer risk
Key weather driver | Sea breeze, RH (BAM bias), inversions | Wind speed (dust), precip scavenging | T (biogenic + evap), photochemistry
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
53 / 60
Notes: One-slide reference sheet comparing the three pollutants side-by-side across the ten dimensions we've covered. Useful as a printable cheat sheet during analysis. Points worth calling out live: (a) PM2.5 is the only pollutant of the three with recent (2024) NAAQS tightening; (b) PM10 has NO annual standard since 2006; (c) VOCs have no NAAQS at all — regulated through ozone/PM NAAQS and HAP NESHAP instead; (d) our Coastal Bend data volume is dominated by CC Palm's 3.3M VOC rows and the PM2.5 hourly BAM sites — everything else is much smaller.

## Slide 57
NEXT STEPS
Next steps for Aidan's PM2.5 / PM10 / VOCs work
1. Method-code audit per site
For each Coastal Bend site x (parameter_code, method_code) tuple, flag AQSIDs whose method_code changes mid-record. Document the transition dates in the methods writeup. Query included in the sensor-evolution slide.
2. Separate 88101 vs 88502 for PM2.5
Rebuild PM2.5 design-value analysis using ONLY parameter code 88101 (regulatory subset). Report both 3-yr rolling and single-year design values. Compare to values in aq.naaqs_design_values.
3. Coastal Bend PM10 audit
Query pipeline for actual PM10 site coverage in Nueces + adjacent. Document data availability by year. Flag any Saharan dust event days for potential Exceptional Events exclusion analysis.
4. CC Palm VOC exploratory descriptives
3.3M rows × 47 species. Start with monthly medians by species, wind-rose CBPFs for benzene + 1,3-butadiene, and diurnal profiles for reactive vs unreactive species. Isoprene as the biogenic check.
5. Weather station pairing for Coastal Bend
Use existing Haversine pairing in aq.site_registry but confirm each pollutant site is paired to a defensible weather station. Sea-breeze proximity matters — a station east of an AQ site sees a different mesoscale regime.
6. Draft methods section
Working from this deck as source material, draft the methods section explicitly identifying FRM/FEM per site, method code transitions, parameter code subsets used for design values, and unit conversions applied (ozone ppb→ppm, VOC ppbC handling).
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
54 / 60
Notes: Six concrete next-step tasks for Aidan's PM2.5 + PM10 + VOCs work, flowing directly from the deck's technical content. In priority order: (1) method-code audit — flag every site with mid-record changes; (2) separate 88101 from 88502 for PM2.5 design-value work (and confirm this against the numbers in aq.naaqs_design_values); (3) PM10 site inventory for Coastal Bend specifically; (4) VOC exploratory descriptives at CC Palm — start with monthly medians, CBPFs, and diurnal profiles; (5) weather-station pairing sanity check; (6) draft methods section from this deck. Manasa's ozone/CO work and Jasmine's SO2/NOx work should follow parallel pipelines with their own dossiers.

## Slide 58
REFERENCES · 1/2
References — foundational literature
Regulatory + methods
40 CFR Part 50 (National Ambient Air Quality Standards) — Appendices A-1, D, F, J, L, O. U.S. Environmental Protection Agency. 40 CFR Part 53 (FEM designation criteria) and Part 58 (monitoring network design). U.S. EPA. 40 CFR Part 63 (NESHAP MACT source-category standards including Subparts CC, UUU, U, R, BBBBBB). U.S. EPA. U.S. EPA (2024, March 6). Reconsideration of the National Ambient Air Quality Standards for Particulate Matter, Final Rule. 89 Fed. Reg. 16202–16406. U.S. EPA (1999, revised 2019). Compendium Method TO-15 / TO-15A. EPA/625/R-96/010b + supplement. U.S. EPA (2025, December 15). List of designated reference and equivalent methods (AMTIC).
PM2.5 health effects
Dockery, D. W., Pope, C. A. 3rd, Xu, X., et al. (1993). An association between air pollution and mortality in six U.S. cities. NEJM, 329(24), 1753–1759. https://doi.org/10.1056/NEJM199312093292401 Pope, C. A. 3rd, Burnett, R. T., Thun, M. J., et al. (2002). Lung cancer, cardiopulmonary mortality, and long-term exposure to fine particulate air pollution. JAMA, 287(9), 1132–1141. https://doi.org/10.1001/jama.287.9.1132 Krewski, D., Jerrett, M., Burnett, R. T., et al. (2009). Extended follow-up and spatial analysis of the American Cancer Society study linking particulate air pollution and mortality. HEI Research Report 140. Di, Q., Wang, Y., Zanobetti, A., et al. (2017). Air pollution and mortality in the Medicare population. NEJM, 376(26), 2513–2522. https://doi.org/10.1056/NEJMoa1702747 Brook, R. D., Rajagopalan, S., Pope, C. A. 3rd, et al. (2010). Particulate matter air pollution and cardiovascular disease. Circulation, 121(21), 2331–2378. Wilker, E. H., Osman, M., & Weisskopf, M. G. (2023). Ambient air pollution and clinical dementia: Systematic review and meta-analysis. BMJ, 381, e071620. Bekkar, B., Pacheco, S., Basu, R., & DeNicola, N. (2020). Association of air pollution and heat exposure with preterm birth, low birth weight, and stillbirth in the US. JAMA Netw Open, 3(6), e208243. IARC (2013). Outdoor air pollution. IARC Monograph 109. WHO (2021). WHO global air quality guidelines: Particulate matter, ozone, NO2, SO2, and CO. Geneva.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
55 / 60
Notes: References part 1 of 2 — foundational regulatory + PM2.5 health literature. Every peer-reviewed citation used in the deck is listed here or on the next slide. APA-formatted with DOIs where available. Users who want to dig into any specific claim can go straight to the primary source. The 89 FR 16202 citation is the 2024 PM2.5 NAAQS revision Federal Register notice — the authoritative reference for the 9 µg/m³ standard.

## Slide 59
REFERENCES · 2/2
References — PM10, dust, VOC / weather
PM10 + Saharan dust + coarse-fraction epidemiology
Adar, S. D., Filigrana, P. A., Clements, N., & Peel, J. L. (2014). Ambient coarse particulate matter and human health: A systematic review and meta-analysis. Curr Environ Health Rep, 1(3), 258–274. Malig, B. J., & Ostro, B. D. (2009). Coarse particles and mortality: Evidence from a multi-city study in California. Occup Environ Med, 66(12), 832–839. Prospero, J. M., & Lamb, P. J. (2003). African droughts and dust transport to the Caribbean: Climate change implications. Science, 302(5647), 1024–1027. Prospero, J. M., & Mayol-Bracero, O. L. (2013). Understanding the transport and impact of African dust on the Caribbean Basin. BAMS, 94(9), 1329–1337. Yu, H., Chin, M., Bian, H., et al. (2015). Quantification of trans-Atlantic dust transport from seven-year CALIPSO lidar measurements. Remote Sens Environ, 159, 232–249. Bozlaker, A., Prospero, J. M., Price, J., & Chellam, S. (2019). Identifying and quantifying the impacts of advected North African dust on PM in Houston/Galveston. J Geophys Res Atmos, 124(22), 12,282–12,300. Bozlaker, A., Contreras, L., Prospero, J. M., & Chellam, S. (2024). Respirable metals, bacteria, and fungi during a Saharan–Sahelian dust event in Houston. Environ Sci Technol, 58(6), 2648–2661. Ortiz-Martínez, M. G., Rodríguez-Cotto, R. I., et al. (2015). Linking endotoxins, African dust PM10, and asthma in Puerto Rico. Mediators Inflamm, 2015, 784212. Tong, D. Q., Wang, J. X. L., Gill, T. E., et al. (2017). Intensified dust storm activity and Valley fever infection in the southwestern United States. Geophys Res Lett, 44(9), 4304–4312. Kaur, K., & Kelly, K. E. (2023). Evaluation of the U.S. EPA's correction equation for PurpleAir sensor data. Atmos Meas Tech, 16(5), 1311–1322.
Weather–pollutant + VOCs
Tai, A. P. K., Mickley, L. J., & Jacob, D. J. (2010). Correlations between fine particulate matter (PM2.5) and meteorological variables. Atmos Environ, 44(32), 3976–3984. Dawson, J. P., Adams, P. J., & Pandis, S. N. (2007). Sensitivity of PM2.5 to climate in the Eastern US. Atmos Chem Phys, 7(16), 4295–4309. Jacob, D. J., & Winner, D. A. (2009). Effect of climate change on air quality. Atmos Environ, 43(1), 51–63. O'Dell, K., Ford, B., Fischer, E. V., & Pierce, J. R. (2019). Contribution of wildland-fire smoke to US PM2.5 and its influence on recent trends. Environ Sci Technol, 53(4), 1797–1804. Burke, M., Childs, M. L., de la Cuesta, B., et al. (2023). Wildfire influence on recent U.S. pollution trends. PNAS, 120(38), e2309325120. TCEQ (2015 rev.). RG-442: Guidelines to Develop Effects Screening Levels, Reference Values, and Unit Risk Factors. TCEQ. Annual Monitoring Network Plans (2018–2024) — Coastal Bend + statewide network.
Melaram Lab · TAMU-CC | South Texas AQ · Coastal Bend briefing
56 / 60
Notes: References part 2. PM10 / Saharan dust literature — Prospero, Bozlaker, Yu, Ortiz-Martínez, Tong, Kaur & Kelly for the low-cost sensor caveat. Weather-pollutant relationships — Tai 2010 is the standard reference for meteorology-PM regression; Dawson 2007 for climate-sensitivity; Jacob & Winner 2009 for climate-change-AQ interactions. O'Dell 2019 and Burke 2023 for the wildfire-driven PM2.5 reversal. TCEQ regulatory docs (RG-442 for ESLs; Annual Monitoring Network Plans for site + instrument history). This is the working bibliography for the entire deck; a manuscript draft can lift these directly.

## Slide 60
MELARAM LAB
South Texas Air Quality Study
Coastal Bend PM2.5 · PM10 · VOCs briefing — v1
Prepared by Aidan Meyers · Melaram Lab, Texas A&M University–Corpus Christi
aidan.meyers@tamucc.edu · www.melaramlab.com
Pipeline: github.com/AidanJMeyers/south-texas-aq-pipeline · v0.4.0
Deck source: 02_Scripts/_deck_build/ · QC feedback welcome
Notes: Closing slide. This deck is the shared baseline for our PM2.5 / PM10 / VOC work — feedback welcome, meant to be iterated on. Regenerate from the pptxgenjs sources under 02_Scripts/_deck_build/ any time we need to update numbers, add a slide, or fix a typo. Manasa and Jasmine can adapt the same skeleton for their pollutants (ozone/CO for Manasa; SO2/NOx for Jasmine).